## Slide 1: The RAS protected bands and use by RA
Tasso Tzioumis (Tasso.Tzioumis@csiro.au)
Australia Telescope National Facility (ATNF)
CSIRO Astronomy and Space Science
SSS2010– Mitaka 31 May – 4 June 2010
Notes: <number>

## Slide 2: Scope
Allocations Table
RAS Allocations
  Extent
Footnote 5.340
Footnote 5.149
Telescope use
Wide-band receivers
SKA 70 MHz – 25 GHz !! - RQZ

## Slide 3: References
Radio Regulations Volume 1 - ITU-R
Radio Astronomy Handbook - ITU-R
  Background and summaries
CRAF Handbook for Frequency Management CRAF Handbook for Radio Astronomy (3rd edition)
  Available free online at http://www.craf.eu/pub.htm
CORF
Handbook of Frequency Allocations and Spectrum Protection for Scientific Uses
  Available free online at
  http://www.nap.edu/catalog.php?record_id=11719

## Slide 4: ITU regions

## Slide 5: Allocations Table - Article 5 - Example
Co-primary allocations; Adjacent bands; OoB emissions
Primary RAS allocation
 Footnotes relevant to RAS
RAS footnote


## Slide 6: Where are the RA bands ?
SUMMARY TABLE:
Frequency Bands(MHz) | Frequency Bands(GHz)
13.360 - 13.410 25.550 - 25.670 37.5 - 38.25 73 - 74.6 150.05 - 153 322 - 328.6 406.1 - 410 608 - 614 1 400 - 1 427 (HI) 1 610.6 - 1 613.8 (OH) 1 660 - 1 670 (OH) 2 655 - 2 700 4 800 - 5 000 (H2CO) | 10.6 - 10.7 14.47 – 14.50 (H2CO)0 15.35 - 15.40 22.21- 22.50 (H2O) 23.6 - 24.0 (NH3) 31.3 - 31.80 42.5 - 43.5 (SiO) 76 - 116 123 - 158.5 164 - 16700 200 - 231.500 241 - 275
Notes: August 4, 2001
AP-RASC '01 - Session J8
<number>

## Slide 7: Details of RAS Allocations – from RAS Handbook
Frequency range (MHz) (1) | Status (2) | Comments (3)
13.36-13.41 | P | 
25.55-25.67 | P (Pas) | 
37.50-38.25 | S | 
73.00-74.60 | P | Region 2
150.05-153.00 | P | Region 1, Australia, India
322.00-328.60 | P | Deuterium line
406.10-410.00 | P | 
606.00-608.00 | P | China and the African broadcasting area
608.00-614.00 | P S | Region 2, India, China and the African broadcasting area Regions 1 (except the African broadcasting area) and 3
1 400.00-1 427.00 | P (Pas) | Hydrogen line
1 610.00-1 613.80 | P | OH line
1 660.00-1 670.00 | P | OH lines
1 718.80-1 722.20 | S | OH line
2 655.00-2 690.00 | S | 
2 690.00-2 700.00 | P (Pas) | 
4 800.00-4 990.00 | S | H2CO line; 4 825-4 835 MHz and 4 950-4 990 MHz are primary in Argentina, Australia and Canada
4 990.00-5 000.00 | P | 

## Slide 8
Frequency range (GHz) (1) | Status (2) | Comments (3)
10.60-10.68 | P | 
10.68-10.70 | P (Pas) | 
14.47-14.50 | S | H2CO lines
15.35-15.40 | P (Pas) | 
22.21-22.50 | P | H2O lines
23.60-24.00 | P (Pas) | NH3 lines
31.30-31.50 | P (Pas) | 
31.50-31.80 | P | Passive in Region 2
42.50-43.50 | P | SiO lines
48.94-49.04 | P | CS line
76.00-77.50 | P | 
77.50-79.00 | S | 
79.00-86.00 | P | 
86.00-92.00 | P (Pas) | SiO lines
92.00-94.00 | P | NH2+ line
94.00-94.10 | S | 
94.10-100.00 | P | CS line

## Slide 9
100.00-102.00 | P (Pas) | 
102.00-109.50 | P | 
109.50-111.80 | P (Pas) | CO lines
111.80-114.25 | P | CO line
114.25-116.00 | P (Pas) | CO line
123.00-130.00 | S | 
130.00-134.00 | P | 
134.00-136.00 | S | 
136.00-148.50 | P | CS line
148.50-151.50 | P (Pas) | 
151.50-158.50 | P | 
164.00-167.00 | P (Pas) | 
182.00-185.00 | P (Pas) | H2O line
200.00-209.00 | P (Pas) | 
209.00-226.00 | P | CO lines
226.00-231.50 | P (Pas) | CO line
241.00-248.00 | P | CS lines
248.00-250.00 | S | 
250.00-252.00 | P (Pas) | 
252.00-275.00 | P | HCN, HCO+ lines

## Slide 10: RAS Allocations notes
Usual mixture of Primary (P) and Secondary (S) allocations
  May vary between ITU-R regions
Most adjacent bands are allocated to active services
  No margin of protection
  Out of band emissions from adjacent or even distant bands
Other co-primary allocations
  Sometimes with active services
Passive primary bands P(passive)
  Allocations only to passive services
  All emissions are prohibited! Footnote 5.340
  But difficult to protect in practice.. What level is “no emission”?

## Slide 11: Footnote 5.340 – No emissions – Passive bands

## Slide 12: RAS Allocation Summary
< 30 GHz:
  1.3% primary exclusive for passive frequency use
  1.2% primary shared allocations
  0.5% secondary allocations
30 - 275 GHz:
  16.8% primary exclusive for passive frequency use
  38.3% primary shared allocations
  5.1% secondary allocations
All frequency bands <275 GHz:
  15.1% primary exclusive for passive frequency use
  34.2% primary shared allocations
  4.6% secondary allocations

## Slide 13: ITU RAS Spectrum - cm wavelengths
In the metre and cm band <1% is allocated to radio astronomy!
Need frequency coverage for redshifted lines
Need bandwidth for continuum sensitivity
Notes: <number>
M. Morimoto
Charm & Crisis in Radio Astronomy
Modern Radio Science 1993

## Slide 14: ITU RAS Spectrum - mm wavelengths
In the mm band the situation is better
But old allocations were not at best frequency
WRC-2000 changes to allocations above 71GHz are a great improvement
Notes: <number>
M. Morimoto
Charm & Crisis in Radio Astronomy
Modern Radio Science 1993

## Slide 15: RA bands above 71 GHz
Notes: August 4, 2001
AP-RASC '01 - Session J8
<number>

## Slide 16: Recommendation RA.314 – Preferred bands
Only a small part of list …
List under review
Many thousands of lines.
Many have no allocation
Redshifted lines also cover most of rest of spectrum…
especially at mm


## Slide 17: Footnote 5.149 – Care but no commitment?

## Slide 18: Footnote 5.565 – above 275 GHz
NOTES:
Revision in WRC-2012 – Agenda item 1.6 – no allocations
Also cover 1-3 THz – New Recommendation RA.1860
Above 3 THz – New area for ITU – IR/Optical

## Slide 19: National Allocations

## Slide 20: Footnote AUS87

## Slide 21: Allocations and Protection
Allocations do not automatically mean protection!!
  Indicate permitted usage but more is needed in practice
National allocations and licensing very important!!
  E.g. in Australia – have to take “Receive licenses”
  Small fees but listed in national database  legal protection
  AUS87 provisions of “notification zones”
    Can work well in practice – co-operative efforts
    Recent example for Methanol lat 6.7 GHz & Transgrid
National sovereignty jealously guarded
  Can go against international allocations!
    Provided no impact on neighbouring nations
Radio quiet zones easiest in National context

## Slide 22: ITU Registration of RAS telescopes
Only via National administration
Include in ITU Master Frequency Register (MFR)
Only accepts registration in allocated bands
Can register national allocations outside RA bands under Article 4.4 (no interference; no protection)
Important for increased visibility of RAS

## Slide 23
Band usage by actual radio-telescopes

## Slide 24: eVLA Bands – 1.2-50 GHz continuous coverage!

## Slide 25: ATCA band usage – most of 1-100 GHz

## Slide 26: Parkes Receivers

## Slide 27: GBT Bands

## Slide 28: Effelsberg Bands

## Slide 29: GMRT Bands

## Slide 30: ALMA bands

## Slide 31: Bands used for RA (VLBI)

## Slide 32: Summary of band usage by RA telescopes
Increasing cover full spectrum !!!
  eVLA: 1-50 GHz continuous; ATCA: most of 1-100 GHz
  SKA: 70 MHz – 25 GHz !!
  ALMA: 100-1000 GHz
Allocated bands covered
  But only a very small part of spectrum
  Is it worth keeping them!!??
YES – Reasons:
  “Islands” for deep observations
  Wider bands built around allocations
  Critical RFI free bands for calibration
  Keeps RAS visible in ITU-R and international for a
Use of remote and radio-quiet zones – SKA; ALMA
RFI mitigation

## Slide 33: Thank you! Questions?
Contact Us
Phone: 1300 363 400 or +61 3 9545 2176
Email: enquiries@csiro.au Web: www.csiro.au
Tasso Tzioumis
Tasso.tzioumis@csiro.au