## Slide 1: ITU-R : its structure, frequency allocations and use in general
3rd Summer School in Spectrum Management
for Radio Astronomy
Mitaka, Tokyo, 31 May – 4 June 2010
Monday, 31 May 2010
HyunSoo Chung
KASI

## Slide 2: Another SS = Spectrum SHARING
IUCAF 3rd SS
Why PROTECION How Free from Interference

## Slide 3
Soon no radio quiet zone on Earth will be free from strong, man-made signals from the sky!!!

## Slide 4: Index
Part I Its Structure
Part II WRC
Part III Frequency Allocations & Use
World Radiocommunication Conferences

## Slide 5
ITU is the leading United Nations agency for information and communication technology issues, and the global focal point for governments and the private sector in developing networks and services. For nearly 145 years, ITU has coordinated the shared global use of the radio spectrum. ITU also organizes worldwide and regional exhibitions and forums, such as WRC, bringing together the most influential representatives of government and the telecommunications
based in Geneva, Switzerland, 191 Member States and more than 700 Sector Members and Associates.
What is ITU?

## Slide 6
Radiocommunication (ITU-R) Managing the international radio-frequency spectrum and satellite orbit resources is at the heart of the work of the ITU Radiocommunication Sector (ITU-R).
Standardization (ITU-T) ITU's standards-making efforts are its best-known — and oldest — activity.
Development (ITU-D) Established to help spread equitable, sustainable and affordable access to information and communication technologies (ICT).
Three ITU Sectors

## Slide 7
Economical
Political Issues
Protection
SHARING
Technical
Study
Radio
Regulations
Gloval
Issues

## Slide 8
Objectives of ITU-R Study Groups
Structure of Study Groups
Radiocommunication Assembly
Scope of Study Groups
Some key areas of standardization
ITU-R Recommendations, Reports and Handbooks
Presentation

## Slide 9
ensure the rational, equitable, efficient and economical use of the radio-frequency spectrum by all radiocommunication services, including passive services(RAS, EESS(passive), SRS(passive) and active services(terrestrial and satellite)
carry out studies without limit of frequency range and adopting Recommendations on radiocommunication matters.
(ref. Article 12 of Constitution)
Role of ITU-R

## Slide 10
Role conducted through (inter alia):
World (and Regional) Radiocommunication Conferences
Approval of Recommendations by Member States
 Technical studies are required which are conducted in Study Groups
Role of ITU-R

## Slide 11: Principal Tasks of ITU-R Study Groups
Develop technical bases for
WRCs (and RRCs)
Develop Recommendations
e.g. CPM process
for WRCs
International voluntary Standards on:
spectrum management, satellite orbits, frequency sharing
system characteristics and operation
ITU-R represents:
International focal point for the standardization
of wireless systems
Compile Reports and Handbooks

## Slide 12: RA-07 - Restructuring Study Groups (1)
SG 1
SG 3
SG 4
SG 6
SG 8
SG 9
SG 1
SG 3
SG 4
SG 6
WP 6S
WP 8D
WPs 8A, 8B, 8F
WPs 9B, 9C, 9D
Spectrum Management
Radiowave Propagation
Satellite Services (FSS+ BSS, MSS & RDSS)
Broadcasting Service
Fixed Satellite Services
Broadcasting Services
Spectrum Management
Radiowave Propagation
SG 7
SG 7
Science Services
Science Services
Former SG structure
New SG structure
Mobile, amateur, radiodetermination and related satellite services
SG 5
Terrestrial Services (fixed, mobile, radiodetermination, maritime, aeronautical, amateur & amateur-satellite)
Fixed Service

## Slide 13: ITU-R Study Groups
Groups of experts (> 1500)from ITU membership
Currently 6 Study Groups
Subordinate groups
  Working Party
  Task Group
  Rapporteur Group
  Joint …….
Coordination Committee for Vocabulary
Special Committee (regulatory/procedural)
CPM - Conference Preparatory Meeting
Member States
Sector Members
Associates
Regional/National
SDO’s
e.g. ETSI, IEC
UN bodies
e.g. WHO, WMO
Industry fora
e.g. WiMAX
Regional Frequency
Management
(APT,, CEPT, CITEL..)
SG 1: Spectrum management
SG 3: Radiowave propagation
SG 4: Satellite services
SG 5: Terrrestrial services
SG 6: Broadcasting service
SG 7: Science services
WP 4A: Orbit/spectrum utilization
WP 7C: Remote Sensing Systems
WP 1C: spectrum monitoring
WP 7D: Radio Astronomy

## Slide 14: ITU-R Study Groups
SG 1: Spectrum management
SG 3: Radiowave propagation
SG 4: Satellite services
SG 5: Terrestrial services
SG 6: Broadcasting service
SG 7: Science services
Supported by Counsellors and Assistants in Study Group Department of BR

## Slide 15: Radiocommunication Assembly
Adopts Study Group work programmes
Approves ITU-R Resolutions
  working procedures
  specific aspects of Study Group responsibility
Approves Recommendations
Establishes ITU-R Study Groups (and elects their chairmen/vice-chairmen)
convened every 3-4 years
associated in time and place with WRCs
(Article 13 of Constitution)

## Slide 16: Study Group 1 Spectrum management
WP 1A - Spectrum engineering techniques
WP 1B - Spectrum management methodologies and economic strategies
WP 1C - Spectrum monitoring
Short Range radio Devices (SRD)
International spectrum regulatory framework

## Slide 17: Study Group 3 Radiowave propagation
WP 3J - Propagation fundamentals
WP 3K - Point-to-area propagation
WP 3L - Ionospheric propagation and radio noise
WP 3M - Point-to-point and Earth-space propagation
Characteristics and mapping of propagation medium
Propagation prediction methods
  e.g. for terrestrial digital broadcasting (RRC-06)

## Slide 18: Study Group 4 Satellite services
WP 4A - Efficient orbit/spectrum utilization for FSS and BSS
WP 4B - Systems, air interfaces, performance and availability objectives for FSS, BSS and MSS, including IP-based applications and satellite news gathering
WP 4C - Efficient orbit/spectrum utilization for MSS and RDSS
Technical characteristics for systems and networks in the RNSS
Satellite radio interface of IMT-2000

## Slide 19: Study Group 5 Terrestrial services
WP 5A - Land mobile service above 30 MHz*(excluding IMT); wireless access in the fixed service; amateur and amateur-satellite services
WP 5B - Maritime mobile service including Global Maritime Distress and Safety System (GMDSS); aeronautical mobile service and radiodetermination service
WP 5C - Fixed wireless systems; HF and other systems below 30 MHz in the fixed and land mobile services
WP 5D - IMT Systems
Joint Task Group 5-6 - Studies on the use of the band 790-862 MHz by mobile applications and by other services
Next generation mobile access “IMT Advanced”
- Spectrum issues for maritime and aeronautical services

## Slide 20: Study Group 6 Broadcasting service
WP 6A - Terrestrial broadcasting delivery
WP 6B - Broadcast service assembly and access
WP 6C - Programme production and quality assessment
Joint Task Group 5-6 - Studies on the use of the band 790-862 MHz by mobile applications and by other services
Sharing issues at UHF
Multimedia and data broadcasting for mobile reception

## Slide 21: Study Group 7 Science services
WP 7A - Time signals and frequency standard emissions
WP 7B - Space radiocommunication applications
WP 7C - Remote sensing systems
WP 7D - Radio astronomy
EESS including meteorological satellite service for
disaster prediction and detection, and for climate monitoring
Protection of passive services, e.g. Radio astronomy

## Slide 22: ITU-R Study Groups on Internet
See: http://www.itu.int/ITU-R/go/rsg

## Slide 23: SG Web Page Structure (using SG 7 as a sample)

## Slide 24: Study Group Products
Technical bases for WRC (and RRC)
    CPM Report
ITU-R Recommendations
Reports and Handbooks

## Slide 25: Table of contents of the CPM Report to WRC-12
1. Maritime and Aeronautical issues
2. Radiolocation and Amateur issues
3. Fixed, Mobile and Broadcasting issues
4. Science issues
5. Satellite issues
6. Future work programme and other issues
Chapters of CPM Report
WRC-12 Agenda items
1.2, 1.19, 2, 4, 8.1, 8.2
1.3, 1.4, 1.9, 1.10
1.14, 1.15, 1.21, 1.23
1.5, 1.8, 1.17, 1.20, 1.22
1.6, 1.11, 1.12, 1.16, 1.24
1.7, 1.13, 1.18, 1.25, 7

## Slide 26: CPM-12 Report Preparation
WP 1A
WP 4A
1.2
1.13
1.6
1.19
WRC-11 (agenda items)
CPM11-2
CPM Management Team Meeting
Draft CPM Report
1.22
WP 1B
WP 4C
1.7
1.18
WP 5A
1.23
1.25
WP 5B
1.3
1.4
1.9
1.10
1.14
1.15
1.21
WP 5C
1.5
1.8
1.20
WP 7B
1.11
1.12
1.24
WP 7C
1.16
JTG 5-6
1.17
SC
7
Technical aspects
Regulatory and procedural aspects
SG-1, SG-4, SG-7
8.1 sub-issues
Chapter 1 (draft texts)
Chapter 2 (draft texts)
Chapter 3 (draft texts)
Chapter 4 (draft texts)
Chapter 5 (draft texts)
Chapter 6* (draft texts)
* includes also a.i. 2, 4, 8.2
CPM Report to WRC-11
SC
Responsible ITU-R Groups

## Slide 27: Study Group Products
Technical bases for WRC (and RRC)
    CPM Report
ITU-R Recommendations
Reports and Handbooks

## Slide 28: ITU-R Recommendation Series
BO: Satellite delivery
BR: Recording for production, archival and play-out; film for television
BS: Broadcasting service (sound)
BT: Broadcasting service (television)
F: Fixed service
M: Mobile, radiodetermination, amateur and related satellite services
P: Radiowave propagation
RA: Radio astronomy
RS: Remote sensing systems
S: Fixed-satellite service
SA: Space applications and meteorology
SF: Frequency sharing and coordination between fixed-satellite and fixed service systems
SM: Spectrum management
SNG: Satellite news gathering
TF: Time signals and frequency standards emissions
V: Vocabulary and related subjects

## Slide 29: Study Group Products
Technical bases for WRC (and RRC)
    CPM Report
ITU-R Recommendations
Reports and Handbooks

## Slide 30: Example Reports from ITU-R
RA.2099
Radio observations of pulsars for precision timekeeping
RA.2126
Techniques for mitigation of radio frequency interference in radio astronomy
RA.2131
Supplementary information on the detrimental threshold levels of interference to radio astronomy observations in Recommendation ITU-R RA.769
RA.2163
Astronomical use of frequency band 50-350 THz and coexistence with other applications

## Slide 31: SG7 Science services Handbooks from ITU-R
Use of Radio Spectrum for Meteorology: Weather, Water and Climate Monitoring and Prediction
Radio Astronomy
Selection and Use of Precise Frequency and Time Systems
Space Research Communications

## Slide 32: Concluding remarks
ITU Radiocommunication Sector represents focal point for standardization of radiocommunication services and systems
The ITU-R Study Groups are the “home” for the technical studies required for the standardization activities
Principal products:
  Technical bases for Radiocommunication Conferences
  Recommendations, Reports and Handbooks

## Slide 33: Role of Itu-R
Part I Its Structure
Part II WRC (Wed., by Gergly)
Part III Frequency Allocations & Use
World Radiocommunication Conferences

## Slide 34: World Radiocommunication Conferences
Updates the Radio Regulations (treaty status)
  Spectrum Allocation
  Coordination and Notification procedures
  Administrative and operational procedures
Adopts Resolutions
Held every 3-4 years
WRC
RR

## Slide 35: Preparation for WRC-12

## Slide 36
2nd Conference Preparatory Meeting (CPM)
 7 month before WRC-12 (prepare CPM Report)
RA(Radiocommunication Assembly, RA-12)  one week before WRC-11
Study of the WRC-12 agenda items
(ITU-R responsible groups (WPs/JTG)
WRC-12 (Geneva, 2012)
31 July 2010
14-25 Feb. 2011
23 Jan. -17 Feb. 2012
16-20 Feb. 2012
Main steps toward WRC-12

## Slide 37: I - WRC within the ITU-R Sector
CPM: Conference Preparatory Meeting
Rec: ITU-R Recommendation
RoP: Rules of Procedure
RR: Radio Regulations (treaty status)
WRC
SC and Study Groups:
SG-1: Spectrum management SG-3: Radiowave propagation SG-4: Satellite services SG-5: Terrestrial services SG-6: Broadcasting service SG-7: Science services
CPM-2
RRB: Radio Regulations Board
SGs: Radiocommunication Study Groups
SC: Special Committee (Regulat. & Procedural)
RA: Radiocommunication Assembly
WRC:World Radiocommunication Conference
Rec
RoP
Radiocommunication Bureau
Director
RRB
Final Acts
ITU Member States (including Regional Groups, Informal Group)
Revisions to RR, Resolutions & Recommendations
Technical bases
Next WRC Agenda
ITU Council
CPM-1
RA

## Slide 38: Regions 1, 2 & 3
May 31, 2010
3rd IUCAF Summer School,Tokyo
<number>
APT
CEPT
CITEL
ATU
RCC
ASMG

## Slide 39: I - WRC Regional Preparation
Six regional groups:
For the preparation of common and coordinated proposals

## Slide 40
Regional preparation for WRC-12
CEPT (European Conference of Postal and Telecommunications Administrations) | 
ATU (African Telecommunications Union) | 
RC C (Regional Commonwealth in the Field of Communications | 
ASMG (Arab Spectrum Management Group) | 
CITEL (Inter-American Telecommunication Commission) | 
APT (Asia-Pacific Telecommunity) | 

## Slide 41: World Radiocommunication Conferences (WRC)
WRC-07 (22.10-16.11.2007)
30 agenda items, 2500 proposal, 3000 del.!
almost all services (terrestrial: FS, MS, BS, Amat.S, RAS, RLS, space: FSS, BSS, MSS, EESS, SRS, SO, MetSat, Amat.Sat)
several applications: IMT, HAPS, HF, GMDSS
WRC-12 (23. 01 – 17. 02. 2012)
- 33 agenda items,
again almost all services (terrestrial: RLS, AM(R)S, passive S, FS, BS, MS, Maritime MS, Amat.S, space: AMS(R)S, SRS, BSS, MSS, MetAids, RDSS, MetSat) and other issues (Res.951, SRDs, Cognitive Radio)
and many applications and systems : UAS, ENG, HAPS, oceanographic radar, …

## Slide 42: Radio Regulations (RR)
The Radio Regulations (treaty status)
incorporates the decisions of the World Radiocommunication Conferences, including all Appendices, Resolutions, Recommendations and ITU-R Recommendations incorporated by reference.
Frequency block allocations to defined radio services (Article 5)
Mandatory or voluntary regulatory procedures (coordination, plan modification, notification, recording) that are adapted to the allocation structure

## Slide 43: Role of ITU-R
Part I Its Structure
Part II WRC
Part III Frequency Allocations & Use
World Radiocommunication Conferences

## Slide 44: Frequency allocatins
<number>
Article 5 Introduction
5.1 In all documents of the Union where the terms allocation, allotment and assignment are to be used, they shall have the meaning given them in Nos. 1.16 to 1.18,
Frequency distribution to | English
Services | Allocation (to allocate)
Areas or countries | Allotment (to allot)
Stations | Assignment (to assign)

## Slide 45: Frequency allocations
<number>
Article 5
5.2 For the allocation of frequencies the world has been divided into three Regions1 as shown on the following map and described in Nos. 5.3 to 5.9:
1 5.2.1 It should be noted that where the words “regions” or “regional” are without a capital “R” in these Regulations, they do not relate to the three Regions here defined for purposes of frequency allocation.

## Slide 46: Regions 1, 2 & 3
May 31, 2010
3rd IUCAF Summer School,Tokyo
<number>

## Slide 47: Worldwide RA frequency committees
<number>
CORF
CRAF
RAFCAP
IUCAF = IAU + URSI + COSPAR

## Slide 48: Worldwide RA frequency committees
<number>
IUCAF : IAU + URSI + COSPAR
Europe -- CRAF
Committee for Radio Astronomy Frequencies
US -- CORF
Committee on Radio Frequencies
AP region -- RAFCAP

## Slide 49: Radio Astronomy Service
ARTICLE 1
Terms and definitions (section 3)
1.58 radio astronomy service: A service involving the use of radio astronomy.
Historically RAS was restricted to ground-based one. Now RAS includes space-based observations.

## Slide 50: Passive & Active Service
Passive services
- RAS, EESS(passive), SRS(passive)
Active services
- See next Tables

## Slide 51: List of the radio services abbreviations
Abbreviations | Radio services | RR definition
AMS | aeronautical mobile service | No. 1.32
AM(R)S | aeronautical mobile (route) service | No. 1.33
AMSS | aeronautical mobile-satellite service | No. 1.35
AMS(R)S | aeronautical mobile-satellite (route) service | No. 1.36
ARNS | aeronautical radionavigation service | No. 1.46
ARNSS | aeronautical radionavigation-satellite service | No. 1.47
AS | amateur service | No. 1.56
ASS | amateur-satellite service | No. 1.57
BS | broadcasting service | No. 1.38
BSS | broadcasting-satellite service | No. 1.39
EESS | Earth exploration-satellite service | No. 1.51
FS | fixed service | No. 1.20
FSS | fixed-satellite service | No. 1.21
ISS | inter-satellite service | No. 1.22
LMS | land mobile service | No. 1.26
LMSS | land mobile-satellite service | No. 1.27
MetAids | meteorological aids service | No. 1.50

## Slide 52: List of the radio services abbreviations
Abbreviations | Radio services | RR definition
MetSat | meteorological-satellite service | No. 1.52
MMS | maritime mobile service | No. 1.28
MMSS | maritime mobile-satellite service | No. 1.29
MRNS | maritime radionavigation service | No. 1.44
MRNSS | maritime radionavigation-satellite service | No. 1.45
MS | mobile service | No. 1.24
MSS | mobile-satellite service | No. 1.25
RAS | radio astronomy service | No. 1.58
RDS | radiodetermination service | No. 1.40
RDSS | radiodetermination-satellite service | No. 1.41
RLS | radiolocation service | No. 1.48
RLSS | radiolocation-satellite service | No. 1.49
RNS | radionavigation service | No. 1.42
RNSS | radionavigation-satellite service | No. 1.43
SOS | space operation service | No. 1.23
SRS | space research service | No. 1.55

## Slide 53: Radio Astronomy in RR
ARTICLE 1
Terms and definitions
1.13 radio astronomy: Astronomy based on the reception of radio waves of cosmic origin
1.5 radio waves or hertzian waves: Electromagnetic waves of frequencies arbitrarily lower than 3 000 GHz, propagated in space without artificial guide.

## Slide 54: Characteristics of emissions
<number>
1.144 out-of-band emission: Emission on a frequency or frequencies immediately outside the necessary bandwidth which results from the modulation process, but excluding spurious emissions.
1.145 spurious emission: Emission on a frequency or frequencies which are outside the necessary bandwidth and the level of which may be reduced without affecting the corresponding transmission of information. Spurious emissions include harmonic emissions, parasitic emissions, intermodulation products and frequency conversion products, but exclude out-of-band emissions.
1.146 unwanted emissions: Consist of spurious emissions and out-of-band emissions.

## Slide 55: OOB & Spurious domains

## Slide 56: Frequency sharing
<number>
1.166 interference: The effect of unwanted energy due to one or a combination of emissions, radiations, or inductions upon reception in a radiocommunication system, manifested by any performance degradation, misinterpretation, or loss of information which could be extracted in the absence of such unwanted energy.
1.169 harmful interference: Interference which endangers the functioning of a radionavigation service or of other safety services or seriously degrades, obstructs, or repeatedly interrupts a radiocommunication service operating in accordance with Radio Regulations (CS).
1.167.1 and 1.168.1 The terms “permissible interference” and “accepted interference” are used in the coordination of frequency assignments between administrations.

## Slide 57: Radio Astronomy Service
ARTICLE 4
Assignment and use of frequencies
4.6 For the purpose of resolving cases of harmful interference, the radio astronomy service shall be treated as a radiocommunication service. However, protection from services in other bands shall be afforded the radio astronomy service only to the extent that such services are afforded protection from each other.
4.7 For the purpose of resolving cases of harmful interference, the space research (passive) service and the earth exploration-satellite (passive) service shall be afforded protection from different services in other bands only to the extent that these different services are protected from each other.

## Slide 58: Primary & Secondary Services
5.23 Primary and secondary services
5.25 a) services the names of which are printed in “capitals” (example: FIXED); these are called “primary” services;
5.26 b) services the names of which are printed in “normal characters” (example: Mobile); these are called “secondary” services (see Nos. 5.28 to 5.31).
5.27 2) Additional remarks shall be printed in normal characters (example: MOBILE except aeronautical mobile).

## Slide 59: Primary & Secondary Services
<number>
5.28 3) Stations of a secondary service:
5.29 a) shall not cause harmful interference to stations of primary services to which frequencies are already assigned or to which frequencies may be assigned at a later date;
5.30 b) cannot claim protection from harmful interference from stations of a primary service to which frequencies are already assigned or may be assigned at a later date;
5.31 c) can claim protection, however, from harmful interference from stations of the same or other secondary service(s) to which frequencies may be assigned at a later date.

## Slide 60: Current Frequency Allocations
<number>
9 kHz – 275 GHz
< 9 kHz :
5.53 Administrations authorizing the use of frequencies below 9 kHz shall ensure that no harmful interference is caused thereby to the services to which the bands above 9 kHz are allocated.
5.54 Administrations conducting scientific research using frequencies below 9 kHz are urged to advise other administrations that may be concerned in order that such research may be afforded all practicable protection from harmful interference.

## Slide 61
Allocation to services |  | 
Region 1 | Region 2 | Region 3
86-92 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 |  | 
92-94 FIXED MOBILE RADIO ASTRONOMY RADIOLOCATION 5.149 |  | 
94-94.1 EARTH EXPLORATION-SATELLITE (active) RADIOLOCATION SPACE RESEARCH (active) Radio astronomy 5.562 5.562A |  | 
94.1-95 FIXED MOBILE RADIO ASTRONOMY RADIOLOCATION 5.149 |  | 
footnotes
Primary alloc.
Secondary alloc.
Current Frequency Allocations

## Slide 62: Important Footnote for RAS
<number>
5.149 In making assignments to stations of other services to which the bands
13 360-13 410 kHz, 25 550-25 670 kHz, 37.5-38.25 MHz, 73-74.6 MHz in Regions 1 and 3, 150.05-153 MHz in Region 1, 322-328.6 MHz, 406.1-410 MHz, 608-614 MHz in Regions 1 and 3, 1 330-1 400 MHz, 1 610.6-1 613.8 MHz, 1 660-1 670 MHz, 1 718.8-1 722.2 MHz, 2 655-2 690 MHz, 3 260-3 267 MHz, 3 332-3 339 MHz, 3 345.8-3 352.5 MHz, 4 825-4 835 MHz, | 4 950-4 990 MHz, 4 990-5 000 MHz, 6 650-6 675.2 MHz, 10.6-10.68 GHz, 14.47-14.5 GHz, 22.01-22.21 GHz, 22.21-22.5 GHz, 22.81-22.86 GHz, 23.07-23.12 GHz, 31.2-31.3 GHz, 31.5-31.8 GHz in Regions 1 and 3, 36.43-36.5 GHz, 42.5-43.5 GHz, 48.94-49.04 GHz, 76-86 GHz, 92-94 GHz, 94.1-100 GHz, | 102-109.5 GHz, 111.8-114.25 GHz, 128.33-128.59 GHz, 129.23-129.49 GHz, 130-134 GHz, 136-148.5 GHz, 151.5-158.5 GHz, 168.59-168.93 GHz, 171.11-171.45 GHz, 172.31-172.65 GHz, 173.52-173.85 GHz, 195.75-196.15 GHz, 209-226 GHz, 241-250 GHz, 252-275 GHz
are allocated, administrations are urged to take all practicable steps to protect the radio astronomy service from harmful interference. Emissions from spaceborne or airborne stations can be particularly serious sources of interference to the radio astronomy service (see Nos. 4.5 and 4.6 and Article 29). (WRC‑07)

## Slide 63: Important Footnote for RAS
<number>
5.340 All emissions are prohibited in the following bands:
1 400-1 427 MHz,
2 690-2 700 MHz, except those provided for by No. 5.422,
10.68-10.7 GHz, except those provided for by No. 5.483,
15.35-15.4 GHz, except those provided for by No. 5.511,
23.6-24 GHz,
31.3-31.5 GHz,
31.5-31.8 GHz, in Region 2,
48.94-49.04 GHz, from airborne stations
50.2-50.4 GHz2,
52.6-54.25 GHz,
86-92 GHz,
100-102 GHz,
109.5-111.8 GHz,
114.25-116 GHz,
148.5-151.5 GHz,
164-167 GHz,
182-185 GHz,
190-191.8 GHz,
200-209 GHz,
226-231.5 GHz,
250-252 GHz. (WRC‑03)
2 5.340.1 The allocation to the Earth exploration-satellite service (passive) and the space research service (passive) in the band 50.2-50.4 GHz should not impose undue constraints on the use of the adjacent bands by the primary allocated services in those bands. (WRC-97)

## Slide 64: Important Footnote for RAS
<number>
5.347A In the bands:
1 452-1 492 MHz, 1 525-1 559 MHz, 1 613.8-1 626.5 MHz, 2 655-2 670 MHz, 2 670-2 690 MHz, 21.4-22 GHz,
Resolution 739 (WRC-03) applies. (WRC-03)

## Slide 65: Important Footnote for RAS
<number>
RESOLUTION 739 (Rev.WRC-07)  created WRC-03
Compatibility between the radio astronomy service and the active space services in certain adjacent and nearby frequency bands
resolves
4 that the radio astronomy stations to be taken into account in applying resolves 1, 2 and 3 are those which are operating in the frequency band(s) identified in Annex 1 and which are notified before the date of reception of the advance publication information of the space station or satellite system to which this Resolution applies;

## Slide 66: Allocation > 275 GHz
<number>
No allocation at present
(only footnote 5.565)
Revision of FN 5.565
– WRC-2012 agenda item 1.6 (up to 3000 GHz)

## Slide 67
May 31, 2010
3rd IUCAF Summer School,Tokyo
<number>

## Slide 68
5.565 The frequency band 275-1000 GHz may be used by administrations for experimentation with, and development of, various active and passive services. In this band a need has been identified for the following spectral line measurements for passive services:
– radio astronomy service: 275‑323 GHz, 327‑371 GHz, 388‑424 GHz, 426‑442 GHz, 453‑510 GHz, 623‑711 GHz, 795‑909 GHz and 926-945 GHz;
– Earth exploration-satellite service (passive) and space research service (passive): 275-277 GHz, 294‑306 GHz, 316‑334 GHz, 342‑349 GHz, 363‑365 GHz, 371‑389 GHz, 416‑434 GHz, 442‑444 GHz, 496‑506 GHz, 546‑568 GHz, 624‑629 GHz, 634‑654 GHz, 659‑661 GHz, 684‑692 GHz, 730‑732 GHz, 851‑853 GHz and 951‑956 GHz.
Future research in this largely unexplored spectral region may yield additional spectral lines and continuum bands of interest to the passive services. Administrations are urged to take all practicable steps to protect these passive services from harmful interference until the date when the allocation Table is established in the above-mentioned frequency band. (WRC‑2000)

## Slide 69
Soon no radio quiet zone on Earth will be free from strong, man-made signals from the sky!!!

## Slide 70: RA bands defined in ITU
<number>
Frequency usages are regulated in ITU
RA bands  rights to be protected

## Slide 71
Thank you!