## Slide 1
<number>
Andrew CLEGG U.S. National Science Foundation aclegg@nsf.gov
Third IUCAF Summer School on Spectrum Management for Radio Astronomy
Tokyo, Japan – June 1, 2010
RF Dialects: Understanding Each Other’s Technical Lingo

## Slide 2: Radio Astronomers Speak a Unique Vernacular
<number>
“We are receiving interference from your transmitter at a level of 10 janskys”
“What the ^#$& is a ‘jansky’?”

## Slide 3: Spectrum Managers Need to Understand a Unique Vernacular
<number>
“Huh?”
“We are using +43 dBm into a 15 dBd slant-pol panel with 2 degree electrical downtilt”

## Slide 4: Why Bother Learning other RF Languages?
<number>
Radio Astronomy is the “Leco” of RF languages, spoken by comparatively very few people
Successful coordination is much more likely to occur and much more easily accommodated when the parties involved understand each other’s lingo
It’s less likely that our spectrum management brethren will bother learning radio astronomy lingo—we need to learn theirs

## Slide 5: Terminology…
<number>
dBm
dBW
V/m
dBV/m
ERP
EIRP
dBi
dBd
C/I
C/(I+N)
Noise Figure
Noise Factor
Cascaded Noise Factor
Line Loss
Insertion Loss
Ideal Isotropic Antenna
Reference Dipole
Others…

## Slide 6: Received Signal Strength
<number>

## Slide 7: Received Signal Strength: Radio Astronomy
<number>
The jansky (Jy):
  1 Jy  10-26 W/m2/Hz
  The jansky is a measure of spectral power flux density—the amount of RF energy per unit time per unit area per unit bandwidth
The jansky is not used outside of radio astronomy
  It is not a practical unit for measuring communications signals
    The magnitude is much too small
    The jansky is a linear unit
  Very few RF engineers outside of radio astronomy will know what a Jy is

## Slide 8: Received Signal Strength: Communications
<number>
The received signal strength of most communications signals is measured in power
  The relevant bandwidth is fixed by the bandwidth of the desired signal
  The relevant collecting area is fixed by the frequency of the desired signal and the gain of the receiving antenna
Because of the wide dynamic range encountered by most radio systems, the power is usually expressed in logarithmic units of watts (dBW) or milliwatts (dBm):
  dBW  10log10(Power in watts)
  dBm  10log10(Power in milliwatts)

## Slide 9: Translating Jy into dBm
<number>
While not comprised of the same units, we can make some reasonable assumptions to compare a Jy to dBm.

## Slide 10: Jy into dBm
<number>
Assumptions
  GSM bandwidth (~200 kHz)
  1.8 GHz frequency ( = 0.17 m)
  Isotropic receive antenna
    Antenna collecting area = 2/4 = 0.0022 m2
How much is a Jy worth in dBm?
  PmW = 10-26 W/m2/Hz  200,000 Hz  0.0022 m2  1000 mW/W = 4.410-21 mW
  PdBm = 10 log (4.410-21 mW) = –204 dBm
Radio astronomy observations can achieve microjansky sensitivity, corresponding to signal levels (under the same assumptions) of –264 dBm

## Slide 11: Jy into dBm: Putting it into Context
<number>
The reference GSM handset receiver sensitivity is –111 dBm (minimum reported signal strength; service is not available at this power level)
A 1 Jy signal strength (~-204 dBm) is therefore some 93 dB below the GSM reference receiver sensitivity
A Jy is a whopping 153 dB below the GSM handset reference sensitivity
A radio telescope can be more than 15 orders of magnitude more sensitive than a GSM receiver

## Slide 12: Other Units of Received Signal Strength: V/m
<number>
Received signal strengths for communications signals are sometimes specified in units of V/m or dB(V/m)
  You will see V/m used often in specifying limits on unlicensed emissions [for example in the U.S. FCC’s Unlicensed Devices (Part 15) rules] and in service area boundary emission limits (multiple FCC rule parts)
This is simply a measure of the electric field amplitude (E)
Ohm’s Law can be used to convert the electric field amplitude into a power flux density (power per unit area):
  P(W/m2) = E2/Z0
  Z0  (0/0)1/2 = 377  = the impedance of free space

## Slide 13: dBV/m to dBm Conversion
<number>
Under the assumption of an isotropic receiving antenna, conversion is just a matter of algebra:
Which results in the following conversions:
(Ohm’s law)

## Slide 14: Conversion Example
<number>
In Japan, the minimum required field strength for a digital TV protected service area is 60 dB(V/m). At a frequency of 600 MHz, this corresponds to a received power of:
P(dBm) = -77.2 + 60 – 20log10(600 MHz) = -73 dBm

## Slide 15: Antenna Performance
<number>

## Slide 16: Antenna Performance: Radio Astronomy
<number>
Radio astronomers are typically converting power flux density or spectral power flux density (both measures of power or spectral power density per unit area) into a noise-equivalent temperature
A common expression of radio astronomy antenna performance is the rise in system temperature attributable to the collection of power in a single polarization from a source of total flux density of 1 Jy:
The effective antenna collecting area Ae is a combination of the geometrical collecting area Ag (if defined) and the aperture efficiency a
  Ae = a Ag

## Slide 17: Antenna Performance Example: Nobeyama 45-m Telescope @ 24 GHz
<number>
Measured gain is ~0.36 K/Jy
Effective collecting area:
  Ae(m2) = 2760 * 0.3 K/Jy = 994 m2
Geometrical collecting area:
  Ag = π(45m/2)2 = 1590 m2
Aperture efficiency = 994/1590 = 63%

## Slide 18: Antenna Performance: Communications
<number>
Typical communications applications specify basic antenna performance by a different expression of antenna gain:
  Antenna Gain: The amount by which the signal strength at the output of an antenna is increased (or decreased) relative to the signal strength that would be obtained at the output of a standard reference antenna, assuming maximum gain of the reference antenna
Antenna gain is normally direction-dependent

## Slide 19: Common Standard Reference Antennas
<number>
Isotropic
  “Point source” antenna
  Uniform gain in all directions
  Effective collecting area  2/4
  Theoretical only; not achievable in the real world
Half-wave Dipole
  Two thin conductors, each /4 in length, laid end-to-end, with the feed point in-between the two ends
  Produces a doughnut-shaped gain pattern
  Maximum gain is 2.15 dB relative to the isotropic antenna

## Slide 20: Antenna Performance: Gain in dBi and dBd
<number>
dBi
  Gain of an antenna relative to an isotropic antenna
dBd
  Gain of an antenna relative to the maximum gain of a half-wave dipole
  Gain in dBd = Gain in dBi – 2.15
If gain in dB is specified, how do you know if it’s dBi or dBd?
  You don’t! (It’s bad engineering to not specify dBi or dBd)

## Slide 21: Antenna Performance: Translation
<number>
The linear gain of an antenna relative to an isotropic antenna is the ratio of the effective collecting area to the collecting area of an istropic antenna:
  G = Ae / (2/4)
Using the expression for Ae previously shown, we find
  G = 0.4 (fMHz)2 GK/Jy
Or in logarithmic units:
  G(dBi) = -4 + 20 log10(fMHz) + 10 log10(GK/Jy)
Conversely,
  GK/Jy = 2.56 (fMHz)-2 10G(dBi)/10

## Slide 22: Antenna Performance: In Context
<number>
Cellular Base Antenna @ 1800 MHz
  G = 2.5 x 10-5 K/Jy
  Ae = 0.07 m2
  G = 15 dBi
Nobeyama @ 24 GHz
  G = 0.36 K/Jy
  Ae = 994 m2
  G = 79 dBi
Arecibo @ 1400 MHz
  G = 11 K/Jy
  Ae = 30,360 m2
  G = 69 dBi

## Slide 23: Other RF Communications Terminology
<number>

## Slide 24: Receiver Noise: Radio Astronomy
<number>
Radio telescope systems utilize cryogenically cooled electronics to reduce the noise injected by the system itself
Usually the noise performance of radio astronomy systems is characterized by the system temperature (the amount of noise, expressed in K, added by the telescope electronics)

## Slide 25: Receiver Noise: Communications Noise Factor and Noise Figure
<number>
Real electronic devices in a signal chain provide gain (or attenuation) which act on both the input signal and noise
  These devices add their own additional noise, resulting in an overall degradation of S/N
Noise Factor: Quantifies the S/N degradation from the input to the output of a system
  F = (S/N)i / (S/N)o
Noise Figure = 10 log (F)

## Slide 26: Noise Factor
<number>
So = GA Si
No = GA Ni + NA
By convention, Ni = noise equivalent to 290 K (Ni = N290 = kB 290 K)
  F = 1 + NA/(GA N290)
For cascaded devices:
  F = FA + (FB-1)/GA + (FC-1)/(GAGB) + …
Compare to the expression of system temperature degradation using cascaded components
  Tsys = TA + TB/GA + TC/(GAGB) + …
Radio astronomy systems have very low NA and high GA, so F is very close to unity
  Noise factor (or noise figure) is not a particularly useful figure of merit for RA systems
GA NA
Si, Ni
So, No

## Slide 27: Quantizing the Noise Level

## Slide 28: Quantizing the Noise Level

## Slide 29: Quantizing the Noise Level

## Slide 30: Quantizing the Noise Level

## Slide 31: Quantizing the Noise Level

## Slide 32: Quantizing the Noise Level
Commercial world describes noise by its amplitude. Radio astronomers describe noise by the accuracy with which you can determine its amplitude.

## Slide 33: S/N, C/I, C/(I+N), etc
<number>
While radio astronomers typically refer to signal-to-noise (S/N), communications systems will often refer to additional measures of desired-to-undesired signal power
C/I
  “C” stands for “Carrier”—the desired signal
  “I” stands for “Interference”—the undesired co-channel signal
  C/I (although written as a linear ratio) is usually expressed in dB
    Example: For a received carrier level of –70 dBm and a received level of co-channel interference of –81 dBm, the C/I ratio is +11 dB.

## Slide 34: S/N, C/I, C/(I+N), etc
<number>
C/(I+N)
  For systems that operate near the noise floor or that have very low levels of interference, the C/I ratio is sometimes replaced by the C/(I+N) ratio, where “N” stands for Noise (thermal noise)
C/(I+N) is a more complete description than C/I

## Slide 35: C/(I+N) Example
<number>
C/(I+N) Example: For a received carrier power of –99 dBm, a received co-channel interference level of –108 dBm, and a thermal noise level within the receiver bandwidth of –115 dBm:
  C = –99 dBm
  I+N = 10 log10(10-108/10 + 10-115/10) = –107 dBm
  C/(I+N) = (–99dBm) – (–107dBm) = +8 dB

## Slide 36: Transmit Power
<number>

## Slide 37: Transmit Power
<number>
The output power of a transmitter is commonly expressed in dBm
  +30 dBm = 1000 milliwatts = 1 watt
There are many things that happen to a signal after it leaves the transmitter and before it is radiated into free space
  Some components of the system will produce losses to the transmitted power
  Antennas may create power gain in desired directions

## Slide 38: A Simple Transmitter System (Cell Site)
<number>
Transmitter #1
Transmitter #2
Combiner
Passband Filter
+43 dBm

## Slide 39: A Simple Transmitter System (Cell Site)
<number>
Transmitter #1
Transmitter #2
Combiner
Passband Filter
Combiner Loss:
At least 10 log N, where N is the number of signals combined
+43 dBm

## Slide 40: A Simple Transmitter System (Cell Site)
<number>
Transmitter #1
Transmitter #2
Combiner
Passband Filter
Insertion Loss:
~ 1dB
-3 dB
+43 dBm

## Slide 41: A Simple Transmitter System (Cell Site)
<number>
Transmitter #1
Transmitter #2
Combiner
Passband Filter
Line Loss:
~ 2 dB
-3 dB
-1 dB
+43 dBm

## Slide 42: A Simple Transmitter System (Cell Site)
<number>
Transmitter #1
Transmitter #2
Combiner
Passband Filter
Antenna Gain
~ +15 dBi
-3 dB
-1 dB
-2 dB
+43 dBm

## Slide 43: A Simple Transmitter System (Cell Site)
<number>
Transmitter #1
Transmitter #2
Combiner
Passband Filter
Total EIRP along boresight:
+52 dBm =
158 W
-3 dB
-1 dB
-2 dB
+43 dBm
+15 dB

## Slide 44: EIRP & ERP
<number>
An antenna provides gain in some direction(s) at the expense of power transmitted in other directions
EIRP: Effective Isotropic Radiated Power
  The amount of power that would have to be applied to an isotropic antenna to equal the amount of power that is being transmitted in a particular direction by the actual antenna
ERP: Effective Radiated Power
  Same concept as EIRP, but reference antenna is the half-wave dipole
  ERP = EIRP – 2.15
Both EIRP and ERP are direction dependent!
  In assessing the potential for interference, the transmitted EIRP (or ERP) in the direction of the victim antenna must be known

## Slide 45: Summary
Radio astronomers must learn the RF terminology commonly used by the rest of the engineering world
Radio astronomers work in linear power units. Everyone else uses logarithmic units
The characterization of “noise” in radio astronomy is different from the rest of the world