## Slide 1: Software Defined Radio and Cognitive Radio Systems
Andrew CLEGG U.S. National Science Foundation aclegg@nsf.gov
Third Summer School on Spectrum Management for Radio Astronomy Tokyo, Japan – June 3, 2010

## Slide 2: Spectrum is a natural resource
Spectrum is:
Finite. Today’s technology can only operate on certain frequencies; commercially viable frequencies are a scarce commodity.
Renewable. Airwaves used to broadcast any transmission can be reused after the broadcast is completed.
Technology dependent. Most natural resources can be harvested manually, albeit inefficiently. Spectrum is in the atmosphere and is usable because technology has been developed to exploit the properties of electromagnetic waves for sound, data and video transmission.
A national asset with international rules and regulations. For example, most domestic uses of spectrum are assigned bands of operation through the International Telecommunication Union, an agency of the United Nations; satellites for broadcasting are governed by international treaty.
Administered. To avoid interference from competing broadcast transmissions, frequency assignments are managed by recognized authorities.

## Slide 3: Opportunistic Spectrum Use
Less than 5% of prime spectrum is used EVERYWHERE and ALL THE TIME  these “white spaces” change with time and location!
Need mechanisms that promote spectrum reuse, sharing, and ancillary secondary markets  And that works for commercial, scientific, and government users
Policy makers need to work proactively with technologists to enable more facile spectrum policies
Source: Paul Kolodzy, Kolodzy Consulting (kolodzy.com)

## Slide 4: Regulatory Activity
REPORT ITU-R SM.2152 (2009)
“Definitions of Software Defined Radio (SDR) and Cognitive Radio System (CRS)”
REPORT ITU-R M.2117 (2007) “Software defined radio in the land mobile, amateur and amateur satellite services”

## Slide 5: Technology Response to the Spectrum Quandary
SDR
  Better spectral efficiencies
  New waveforms
CRS
  In some cases enabled by SDR
  Spectrum Reuse possibilities
  Awareness of under utilized spectrum
    Dynamic Reconfiguration of radio and advantageous use of assignments

## Slide 6: Ongoing SDR and CRS International Research
Government and Regional sponsored projects
  Canada, China, Japan, EU
Standards Bodies
  IEEE
Industry Groups
Academia
Advances in software defined radio and cognitive radio systems
may in time change the nature of spectrum allocation policies

## Slide 7: Definition of Software Defined Radio (SDR)
“Software-defined radio (SDR): A radio transmitter and/or receiver employing a technology that allows the RF operating parameters including, but not limited to, frequency range, modulation type, or output power to be set or altered by software, excluding changes to operating parameters which occur during the normal pre-installed and predetermined operation of a radio according to a system specification or standard.”

## Slide 8: SDR
The progression of hardwired functions to software running on processors is the natural evolution of digital applications
  Audio functions migrated from DSPs to CPU
  Modems migrated to “soft” modems
  Correlators migrating from delay cables to ASICs to CPUs and FPGAs
Typically when it happens is a function of cost/flexibility: as number of radio interfaces increases it will become more economical to switch

## Slide 9: Architectures of SDR
SDR Architecture Based on Current-Generation Technology
Notes to Figure 1:
  DUC: Digital upconverter DDC: Digital downconverter
  CFR: Crest factor reduction DPD: Digital predistortion
  PA: Power amplifier LNA: Low noise amplifier

## Slide 10: Definition of Cognitive Radio System (CRS)
“Cognitive radio system (CRS): A radio system employing technology that allows the system to obtain knowledge of its operational and geographical environment, established policies and its internal state; to dynamically and autonomously adjust its operational parameters and protocols according to its obtained knowledge in order to achieve predefined objectives; and to learn from the results obtained.”

## Slide 11: Methods of obtaining knowledge for CRS
Collecting information from components of CRS
Geo-location awareness
Spectrum sensing
Database access (central or distributed)
Listening to a wireless channel
Collaboration between different radio systems

## Slide 12: Technical characteristics and capabilities of CRS
The three technical features that characterize a CRS are:
1) the capability to obtain the knowledge of its radio operational and geographical environment, its internal state, and the established policies, and to monitor usage patterns and users’ needs, for instance, by sensing a spectrum, using a database, and receiving control and management information;
2) the capability to dynamically and autonomously adjust its operational parameters and protocols according to this knowledge in order to achieve predefined objectives, e.g. more efficient utilisation of spectrum; and
3) the capability to learn from the results of its actions in order to further improve its performance.

## Slide 13: Background

## Slide 14
N
.
$$
$
¢
$$$
Low cost – high volume
Ubiquitous devices which MAY be AUTHORIZED to operate in many dimensions BUT may have internal system limitations.
Could be a software controlled LEGACY Radio with minimal advanced technology.
Follows orders from something like a PILOT CHANNEL!
Higher capability
Reads the PILOT CHANNEL data and may be able, if AUTHORIZED, to operate in many configurations or dimensions.
Environment Aware
May be able to identify location from peer network or LBS/GPS capabilities. Solicits operating rule set data from its network or internal database and operates in conformance with that information.
Autonomous
Senses RF environment.
Conforms with rule set(s) from internal database and operates in conformance with that information. Advanced capability to reconfigure RF operations
Cognitive System Hierarchy
Cost vs. Capability
NIRVANA – STEALTH – NIB

## Slide 15: Policy-Defined, Cognitive Radios
Cognitive devices that
  Are Aware
    Of itself, its capabilities, its health, etc.
    Of its environment
    Of the effects of its actions
  Can Reason
    At different levels of abstraction using goals, policies, and models of its capabilities and environment
    To determine behavior (sensing, evaluation, transmission)…
  Can Adapt
    To new business goals, policies, …
  Can Learn
    Better strategies, refined models
    Are Able To Cooperate and Coordinate with peers
      for mutual benefit
      to achieve overall goal
Notes: <number>

## Slide 16: Dynamic Spectrum
DS ALLOCATION
  Opportunistic use of a resource pool of frequency assignments
    Under license with liberalized use rules
DS ACCESS
  Oppotunistic use of spectrum observed or otherwise identified as ‘available’
    Sensing
    Pico Auctions

## Slide 17: Dynamic Spectrum Access Etiquettes
    Listen Before Talk.
    Least Interfered Channel.
    Fixed/Variable Frame Time Division.
    Transmit Power Control.
    Dynamic Frequency Selection.
    Location Dependent Spectrum Access.
    Time Dependent Spectrum Access.
    Mobility Dependent Spectrum Access.
    Permission (Positive/Negative Control) Dependent Spectrum Access
    Duty Cycle Dependent Spectrum Access.
    Protocol Dependent Spectrum Access.

## Slide 18: WRC-12 Agenda Item 1.19
1.19 to consider regulatory measures and their relevance, in order to enable the introduction of software-defined radio and cognitive radio systems, based on the results of ITU‑R studies, in accordance with Resolution 956 (WRC‑07)
  Resolution 956 (WRC-07): Regulatory measures and their relevance to enable the introduction of software-defined radio and cognitive radio systems.

## Slide 19: SDR/CRS and Radio Astronomy

## Slide 20: Challenges
    Coherent non-blanking RFI excision algorithms often require knowledge of interfering waveform
      SDR can change waveforms at will, possibly complicating automated excision efforts
    Wholesale abandonment of allocations, allotments, and “command and control” licensing could complicate predictions of the RFI environment in which we operate
    Cognitive radios cannot autonomously sense the presence of a channel occupied by a passive service
    The use of beacons or control channels to signal spectrum use would itself require more transmitters, possibly in otherwise “quiet” zones
    Hacking of SDR and CRS could create spectrum chaos – security is needed

## Slide 21: Opportunities
    SDR and CRS are very likely the future of radio – we need to adapt
    Radio astronomers have some experience with cognitive radio
      Opportunistic out-of-band observing
      Dynamic scheduling
    Perhaps we can share some of our experiences with the CRS community
    The adoption of SDR and CRS technologies is expected to be governed on a national and/or regional level
      Be sure to contribute to relevant rulemakings, standards work, etc.
    Perhaps wide scale adoption of CRS techniques might actually improve our ability to observe out-of-band

## Slide 22: Resources
    Wireless Innovation Forum (formerly the SDR Forum)
      http://www.wirelessinnovation.org
    IEEE Standards Coordinating Committee 41 (Dynamic Spectrum Access Networks)
      http://grouper.ieee.org/groups/scc41/index.html (main page)
      http://grouper.ieee.org/groups/scc41/crinfo/ (Cognitive Radio Information Center)