## Slide 1: Coordination with Satellites
(Cloudsat, LEOs, etc.)

## Slide 2: Outline
I. Regulatory Requirements
- RR Article 11
- RR Article 9
(- RR Appendices 30, 30A, 30B)
II. Coordination in Practice
- subject / not subject to coordination
- RR 4.4
- RR Appendix 4
- examples of inter-agency coordination
III. Spirit of Coordination
- spectrum as generally available resource
- coordination: cooperation rather than confrontation
- good examples, bad examples

## Slide 3: Regulatory Requirements Radio Regulations, ARTICLE 11
Notification and recording of frequency assignments
Any frequency assignment .... shall be notified to the Bureau:
if the use of that assignment is capable of causing harmful interference to any service of another administration; or
if that assignment is to be used for international radiocommunication; or
if that assignment is subject to a world or regional frequency allotment or assignment plan which does not have its own notification procedure; or
if that assignment is subject to the coordination procedure of Article 9 or is involved in such a case; or
if it is desired to obtain international recognition for that assignment; or
if it is a non-conforming assignment under No. 8.4 and if the administration wishes to have it recorded for information.

## Slide 4: Regulatory Requirement Radio Regulations, ARTICLE 9
Procedure for effecting coordination with or obtaining agreement of other administrations
Article 9 contains
- lists of cases, in which coordination is mandatory,
- the advance publication and coordination procedures,
- the due dates for the different kind of information or actions.
Article 9 describes the processes of
- advance publication
- coordination
- notification

## Slide 5: Regulatory Requirement Radio Regulations, ARTICLE 9
Coordination is mandatory ("subject to coordination"):
3-stage process for all satellites on geostationary orbit and for NGSOs in cases, when the requirement to coordinate is included in a footnote
- fairly simple advance publication information
- extensive coordination request
- request for notification after successful coordination
Coordination is not mandatory ("not subject to coordination"):
2-stage process for most satellites in non-geostationary orbit
- extensive advance publication information
- request for notification

## Slide 6: Regulatory Requirement Radio Regulations, ARTICLE 9
Earth observation or space research satellites are "not subject to coordination" (unless they are in GSO, e.g. relay satellites)
such satellites will be notified and entered into the master register without completing a formal coordination procedure
"coordination light" takes place based on the advance publication information.

## Slide 7: Regulatory Requirement Radio Regulations, Appendicees 30, 30 A, and 30 B
ITU has two coordination approaches:
- first come - first served
- planned bands
some frequency bands in the FSS, BSS and associated feeder links are treated as "planned bands" and procedures different from Article 9 apply
not relevant for science services

## Slide 8: Coordination in Practice subject / not subject to coordination

## Slide 9: Coordination in Practice subject / not subject to coordination

## Slide 10: Coordination in Practice subject / not subject to coordination
For satellites not subject to coordination the process of "coordination light" starts with the advance publication, which contains the necessary technical information.
For satellites subject to coordination the advance publication only contains the orbital position and the frequency bands (allocations) and is for information only. Coordination starts after the next step, the "Coordination Request", which is very detailed.

## Slide 11: Coordination in Practice RR 4.4

## Slide 12: Coordination in Practice RR 4.4
Radio Regulations, Article 4
The case of assignements not in conformity with the frequency allocation tables is explicitely forseen.
Administrations are free to deviate from the Radio Regulations as long as no harmful interference is caused.

## Slide 13: Coordination in Practice RR Appendix 4 The parameters to be provided for publication and coordination are detailed in:

## Slide 14: Coordination in Practice RR Appendix 4

## Slide 15: Coordination in Practice RR Appendix 4

## Slide 16: Coordination in Practice RR Appendix 4

## Slide 17: Coordination in Practice RR Appendix 4

## Slide 18: Coordination in Practice RR Appendix 4
The Coordination process looks at systems operating in the same frequency band with overlapping frequencies.
Interference due to unwanted emissions are not generally considered.
Exemption: footnotes containing flux density limits against services in neigbouring bands.
Administrations may always comment and ask for coordination, even in cases, which are not detailled in Article 9, e.g. filings under RR 4.4

## Slide 19: Coordination in Practice RR Appendix 4
Coordination based on Article 9 RR is a matter of the administrations of ITU-member states.
The ITU-R is involved and keeps track of the coordination processes.
Practical work is done by the operators of a satellite system, administrations may assist if required.
Operators of conflicting satellite assignments negotiate until they come to an agreement.
The details of the agreement are normally kept secret. Non-disclosure agreement!!!

## Slide 20: Coordination in Practice examples of inter-agency coordination
Satellite systems of space agencies normally not subject to coordination
To avoid harmful interference, space agencies discuss their planned missions in advance of the ITU filing process
SFCG has database with all agency missions and responsible contact person
SFCG has adopted resolution for inter-agency coordination
In some cases operational coordination is necessary (and done!)

## Slide 21: Coordination in Practice examples of inter-agency coordination
Examples for operational coordination:
TerraSAR must not transmit telemetry data in S-band in certain sections of a few orbits in oder not to cause harmful interference to some Russian and Japanese geostationary satellites.
One experimental transmitter onboard the ISS has the potential to cause harmful interference to one ESA satellite on polar orbit: Before any run of the experiment the orbital positions are checked relative to the ESA ground station.

## Slide 22: Coordination in Practice examples of inter-agency coordination
Agencies may also consider unwanted emissions for coordination cases.
Example: CloudSat
CloudSat is "not subject to coordination" and no fixed pfd limit given in a footnote, therefore coordination between agencies, only. No administration involved.
Cloudsat is example of operational coordination.

## Slide 23: Coordination in Practice examples of inter-agency coordination

## Slide 24: Coordination in Practice examples of inter-agency coordination
5.562 The use of the band 94-94.1 GHz by the Earth exploration-satellite (active) and space research (active) services is limited to spaceborne cloud radars. (WRC-97)
5.562A In the bands 94-94.1 GHz and 130-134 GHz, transmissions from space stations of the Earth exploration-satellite service (active) that are directed into the main beam of a radio astronomy antenna have the potential to damage some radio astronomy receivers. Space agencies operating the transmitters and the radio astronomy stations concerned should mutually plan their operations so as to avoid such occurrences to the maximum extent possible. (WRC‑2000)

## Slide 25: Coordination in Practice examples of inter-agency coordination
...
...
...

## Slide 26: Coordination in Practice examples of inter-agency coordination

## Slide 27: Spirit of Coordination Spectrum as generally available resource
Director of ITU Radio Bureau to WP7D: "I want the spectrum to be used!"
Radioastronomers were shocked!
What he probably meant was: The radio spectrum is a natural resource available to all mankind. Nobody should block spectrum.
The same director later accused satellite operators of "massive overfiling".
The spectrum is divided into allocations, but no administration, no service , and no operator has property rights of any part of the spectrum.
By overfiling satellite operators try to gain excluve rights over part of the spectrum, without actual need.

## Slide 28: Spirit of Coordination Spectrum as generally available resource
Filing under RR 4.4: It is not forbidden to assign frequencies in a non-complient way.
One purpose of the Radio Regulations is to avoid harmful interference, and the allocation table of Article 5 is the most recommended means. If harmful interference can be avoided by other means, administrations are free to use these other means.
Stricly applying the Radio Regulations incl. Article 5 does not guarantee interference-free operation, as radioastronomers are very well aware.
Particular problem: Unwanted emissions.

## Slide 29: Spirit of Coordination Coordination: cooperation rather than confrontation
94 GHz EESS (active) vs. Radioastronomy is basically an unwanted emission problem.
Other bands for high-power transmissions from EESS (active) exist, where distance to RA allocation is much larger.
On request by IUCAF, the space agencies consider similar resolution to protect radioastronomy also in other bands.

## Slide 30: Spirit of Coordination Coordination: cooperation rather than confrontation

## Slide 31: Spirit of Coordination Coordination: cooperation rather than confrontation
The European space agencies work together in ECSS on a set of norms and regulations on:
- Space Project Management
- Space Product Assurance
- Space Engineering
They commit themselves to obbey to these rules.

## Slide 32: Spirit of coordination good examples, bad examples

## Slide 33: Spirit of coordination good examples, bad examples

## Slide 34: Spirit of coordination good examples, bad examples

## Slide 35: Spirit of coordination good examples, bad examples

## Slide 36: Spirit of coordination good examples, bad examples

## Slide 37: Spirit of coordination good examples, bad examples
European Space Agencies shall oblige there manufacturers to meet these limits.
Some European satellite manufacturers have taken over the ECSS requirements.
AfriSat was built by such a European manufacturer, however:
When AfriSat was switched on, the sky became apparently radio-bright also over Europe.

## Slide 38: Spirit of coordination good examples, bad examples
The orbital position of AfriSat, observed in a passive frequency band.
Intermodulation products were excluded, because the receiver was checked to be linear.

## Slide 39: Spirit of coordination good examples, bad examples
The orbital position of AfriSat, observed in a passive frequency band, after filtering.
Also in this case, the receiver was, of course, linear!

## Slide 40: Spirit of coordination good examples, bad examples
Same band, same telescope:
Observers complained about intermittend interference in the passive 21 cm band after DAB-T was put into operation in the band 1452-1492 MHz.
A test campaign was run one night, in close cooperation with the operator of the broadcast stations. Stations were switched off and on again and the interference situation was checked with an simulated observational run.
There was no obvious improvement while any of the 3 nearest stations was switched off.
The operator could be persuaded to switch off all 3 stations at the same time, with no clear improvement in the observational data.
While all 3 broadcast stations were switched off, the radio telescope was moved to point as closely as possible towards the observatory building.
The source of interference in the passive band was immediately identified!

## Slide 41: Spirit of coordination good examples, bad examples
And now the bad example part:
The internet site of the radio observatory in question maintained a page with technical news and information, visible from the outside world.
On this page the notice was found that 21 cm observations were severely hampered by interference due to digital audio broadcasting.
This notice was not removed for a very long time, even though the frequency manager, who had organised the test campaign, asked for it by telefone, emails and even in writing.

## Slide 42: Conclusion
All radio services have the right to use the spectrum.
All services should respect each other and try to understand each other, and this is not just a matter of "lingo".
Problems will occur, and can be solved or mitigated only through cooperation.