## Slide 1
<number>
Andrew CLEGG U.S. National Science Foundation aclegg@nsf.gov
Third Summer School on Spectrum Management for Radio Astronomy Tokyo, Japan – June 3, 2010
Digital TV and Its Impact on Radio Astronomy

## Slide 2: Analog Television Terrestrial Broadcasting Standards
<number>
Abbrev | Name | Main Geographic Use
PAL | Phase Alternating Line | Most of Europe, Australia, Parts of Asia (including India & China), Most of Africa, Eastern South America
NTSC | National Television System Committee | North & Central America, Western South America, Japan, Philippines, Thailand, Taiwan, South Korea
SECAM | Sequential Color with Memory | France, Russia & former Soviet republics, portions of Africa, Madagascar

## Slide 3: Analog TV Standards Worldwide
<number>

## Slide 4: Digital Television Worldwide
Worldwide, terrestrial TV broadcasts are switching from analog to digital modulation
  Different countries have different schedules for switching over (most by 2015)
  Some satellite TV broadcasting has been digital for more than 15 years
Japan is deploying ISDB-T technology, replacing NTSC and analog HDTV MUSE standards
  ISDB-T also being widely deployed in South America
North America is deploying ATSC digital TV to replace NTSC analog standard
  U.S. digital transition is completed for “full-service” broadcasts; legacy NTSC remains for low-power stations
Australia and Europe are deploying DVB-T
China is rolling its own (DMB-T)
<number>

## Slide 5: Digital TV Terrestrial Broadcasting Standards
<number>
Abbrev | Name | Over-the-Air Modulation Type | Main Geographic Use
DVB-T | Digital Video Broadcasting – Terrestrial | Coded Orthogonal Frequency Division Multiplexing (COFDM) (QPSK, 16QAM, and 64QAM) | Europe, Russia, Australia, Parts of Asia
ISDB-T | Integrated Services Digital Broadcasting - Terrestrial | Coded Orthogonal Frequency Division Multiplexing (COFDM) (DQPSK, QPSK, 16QAM, and 64QAM) | Japan, South America (ISDB-T International)
ATSC | Advanced Television Systems Committee | 8-level Vestigial Sideband (8VSB) | North America, South Korea
DMB-T/H | Digital Multimedia Broadcast – Terrestrial/ Handheld | Time Domain Synchronous Orthogonal Frequency Division Multiplexing (TDS-OFDM) | China only

## Slide 6: Digital TV Standards Worldwide
<number>

## Slide 7: Digital Transition Worldwide
<number>
Completed, no analog / Completed for full-service stations / In transition / Planned / No transition planned / No Information

## Slide 8: TV Spectra
<number>
DVB-T (OFDM)
ISDB-T (Yellow) (OFDM)
Digital
Analog
PAL / SECAM / NTSC Generic
(All have video, chrominance, and audio carriers. Some differences in total bandwidth and frequency offset between carriers.)
ATSC (8-VSB)
PAL

## Slide 9: Maximum Transmit Power (U.S.)
<number>
Chan | Freq (MHz) | Maximum Analog EIRP (kW) | Maximum Digital EIRP (kW)
2 – 6 | 54 – 72 & 76 – 88 | 164 | 74
7 – 13 | 174 – 216 | 518 | 262
14 – 51 | 470 – 698 | 8222 | 1640

## Slide 10: DTV Unwanted Emissions Limits (U.S.) (Assumes full-power 1640 kW EIRP)
<number>

## Slide 11: Comparison of Analog (NTSC) and Digital (ATSC) TV Signal Spectra
<number>
Direct comparison of digital (8-VSB modulation, left) and analog (AM-VSB, PM, and FM, right) TV signals, of the same station from the same tower at the same time. The analog signal has more power because of the large video carrier, but the digital signal fills in the spectrum completely.

## Slide 12: Comparison of Digital (ATSC) and Analog (NTSC) Signals
<number>

## Slide 13: Ratio of Power Spectral Density of Digital (ATSC) to Analog (NTSC)
<number>

## Slide 14: Ratio of Power Spectral Density of Digital to Analog (detail)
<number>
For equivalent digital and analog TV signals, the digital power spectral density exceeds the analog PSD over 94% of the bandwidth, and by as much as 3 orders of magnitude.

## Slide 15: How to Identify TV Signal

## Slide 16: Digital and Analog TV in Mitaka
Japanese NTSC TV broadcast on channel 3 (102 – 108 MHz).
Video carrier (103.25 MHz)
Color carrier
(106.78 MHz)
Audio carrier
(107.75 MHz)
Japanese ISDB-T broadcasts on channels 25, 26, & 27 (542 – 560 MHz)
Channel 26 (548 – 554 MHz)
Channel 25 (542 – 548 MHz)
Channel 27 (554 – 560 MHz)

## Slide 17: Observational Comparison of Digital and Analog TV Interference
<number>

## Slide 18: Television Interference Caused by Anomalous Propagation at the Murchison Widefield Array Site
<number>
Digital TV signal in Australian channel 7 (181 – 188 MHz), and narrowband interference from analog (PAL) luminance, chrominance, and audio carriers of channels 6 (174 – 181 MHz), 8 (188 – 195 MHz), and (partially) 9 (195-202 MHz). The digital TV signal is believed to be arising from a distance of 290 km during a period of anomalous propagation. Data obtained in March 2010.

## Slide 19: TV Broadcasts and Rec. 769
<number>

## Slide 20: Digital TV and Redshifted HI
<number>

## Slide 21: Worldwide Lower VHF Channel Plans
<number>
Figure from Wikipedia, based on data from “World Analogue Television Standards and Waveforms” (http://www.pembers.freeserve.co.uk/World-TV-Standards/Transmission-Systems.html)

## Slide 22: Worldwide Upper VHF Channel Plans
<number>
Figure from Wikipedia, based on data from “World Analogue Television Standards and Waveforms” (http://www.pembers.freeserve.co.uk/World-TV-Standards/Transmission-Systems.html)
See color key on previous slide

## Slide 23: Comparison of Analog and DTV Channel Allotments
<number>
Allotments specify which channels are available for use in each city or market area
  Allotments are based on market size, co- and adjacent-channel interference criteria, geography, frequency, and other considerations
Given the lucrative nature of a TV license, virtually all allotted channels are spoken for
There are significant differences between the DTV allotments after the transition and the analog allotments prior to the transition
A comparison of the allotment tables provides a quick snapshot of the imminent changes in the spectrum landscape.

## Slide 24: Analog TV Allotments Before DTV Transition
<number>

## Slide 25: Digital TV Allotments After DTV Transition
<number>

## Slide 26: Difference between Digital and Analog TV Allotments
<number>

## Slide 27: Summary
The world is switching to digital terrestrial TV broadcasting
Digital TV produces more apparent interference than analog TV
Both digital TV and (in some countries) the refarming of TV broadcast spectrum will make observations using TV band frequencies more challenging
TV interference is most disruptive to the search for highly redshifted HI, such as the search for the Epoch of Reionization (EOR)
TV interference in general, and digital TV interference in particular, have been shown to impact radio observatories hundreds of km from the transmitting source
Radio astronomers can generally not expect any regulatory protections when using TV spectrum for observing
Future instruments such as the SKA must take TV interference into account
<number>