## Slide 1: Impact to the Radio Astronomy by the Interference caused by the Solar Power Satellite Systems
Masatoshi Ohishi
NAOJ

## Slide 2: SSPS
Power Generation in Space (GSO)
Power transmission via microwave beam
Rectenna on earth ground

## Slide 3: Pros and Cons
Can generate 24/24
No CO2 emissions
Economic
  cheaper than nuclear power plant
Unlimited energy source
others
Interference to radiocomm. Including RAS
Burn out “birds”
Unknown effect to ionosphere
Costs too much
  Sat. has life-time
others

## Slide 4: SSPS frequencies
ISM band; 2.45 GHz / 5.8 GHz
Monotonic – actual bandwidth (df) ??
Harmonics may fall into the RAS bands  occupied bandwidth = n x df
  2.45GHz: x2, x6, x9, x20
  5.8 GHz: better than 2.45 GHz case
  Both: 76-116 GHz

## Slide 5: ISM bands/applications
13,553-13,567 kHz, 26,957-27,283 kHz, 40.66-40.70 MHz, 902-928 MHz in Region 2, 2,400-2,500 MHz, 5,725-5,875 MHz, and 24-24.25 GHz
RR 15.13 Administrations shall take all practicable and necessary steps to ensure that radiation from equipment used for industrial, scientific and medical applications is minimal and that, outside the bands designated for use by this equipment, radiation from such equipment is at a level that does not cause harmful interference to a radiocommunication service and, in particular, to a radionavigation or any other safety service operating in accordance with the provisions of these Regulations.

## Slide 6: Appendix to Article 3
Tables of maximum permitted power levels for spurious or spurious domain emissions
Attenuation (dB) below the power supplied to the antenna transmission line: 43 + 10 log (P), or 70 dBc, whichever is less stringent P = 1GW = 109W 43 + 10 log (P) = 943 > 70  100 W  such power may burn out RAS Rx !

## Slide 7: Spectral purity
The bandwidth for the transmission (df) must be as narrow as possible to avoid interference detrimental to the RAS.
The harmonics/intermodulations must be suppressed in order not to cause unacceptable interference to the RAS.

## Slide 8: Detrimental thresholds for total power observations
Black: continuum
Red: spectral line
Recommendation ITU-R RA.769

## Slide 9: Extremely low far sidelobe
The sidelobe of the transmitting antenna must also be as low as possible to avoid serious damage to the RAS antenna.
df=1MHz(?)
peak: ~30mW/cm2  -35dBW/m2/Hz
1st SD: 0.1mw/cm2  -60dBW/m2/Hz
RA.769
spfd = (-250 ~ -230) dBW/m2/Hz

## Slide 10: Sky occupied by SSPSs
1GW / satellite
1 TW (or more)  1000 satellites
GSO – every 2 degrees  360/2 = 180 satellites  1000 - 180 = 820 satellites are not in the GSO  NGSO (HEO ?)

## Slide 11: Interference by GSOs
GSOs
21cm obs. at Bonn

## Slide 12: Projection of the geostationary orbit onto the celestial sphere as seen from a number of radio observatories
RA Handbook Fig. 4.3 (p. 45)

## Slide 13: Other orbits than GSO ?
Highly Elliptical Orbit (HEO) Satellite
Projected orbit
Too many spots
on the sky !

## Slide 14: Interference to optial/IR astronomy
10x10 km2 solar cell  ~ 1 arcmins  larger than Jupiter (~40 arcsecs) permanent blocking
Reflection of the solar light

## Slide 15: Summary
SSPSs may cause interference detrimental to the radio/IR/optical astronomy.
Spectrum purity, very low sidelobe are crucial to minimize the problems.
NY times July 23, 2008
?