## Slide 1: Coordination in the APT
3rd Summer School in Spectrum Management
for Radio Astronomy
Mitaka, Tokyo, 31 May – 4 June 2010
Thursday, 3 June 2010
HyunSoo Chung
KASI

## Slide 2
Before Presentation
Freedom is not FREE
Change is not FREE
Protection is not FREE
Dream
IF YOU WANT TO SUCCESS,
YOU MUST HAVE TO CHALLENGE
Motivation
NO Money, NO Problem
 NO Problem, NO Spirit
NO Problem, No Protection

## Slide 3: Coordination in APT
Part I General Status
Part II Related Issues

## Slide 4: Regions 1, 2 & 3
May 31, 2010
3rd IUCAF Summer School,Tokyo
<number>
APT
CEPT
CITEL
ATU
RCC
ASMG

## Slide 5: Asia-Pacific RA Telescopes-1
<number>
Australia
Radio astronomy stations operating in the Asia-Pacific Region |  |  |  |  |  | 
Country | Site | Longitude (East) | Latitude (North) | Operating Frequency (M/GHz) | Diameter (m) | Remarks
Australia | Parkes | 148º 15' 44" | –33º 00' 00" | 440 M, 640-704 M 1.2-1.8, 2.2-2.5, 2.6-3.6, 4.5-5.1, 5.9-6.8, 8.1-8.7, 12-15, 21-24GHz | 64 | S,VLBI
 | Mopra | 149º 05' 58" | –31º 16' 04" | 1.2-1.8, 1.8-3.0, 4.4-6.7, 8.0-9.2, 16-25, 83.5-116, Hz | 22 | S,VLBI
 | ATCA (Narrabri) | 149º 32' 56" | –30º 59' 52" | 1.25-1.78, 2.2-2.5, 4.4-6.7, 8.0-9.2, 16-25, 83.5-106GHz | 6  22m | I, VLBI
 | Tidbinbilla | 148º 58' 59" | –35º 24' 18" | 1.61-1.705, 2.2-2.3, 8.1-8.6, 19-24.3, | 70m, 34m | S,VLBI
 | Hobart (Mt. Pleasant) | 147º 26' 21" | –42º 48' 18" | 1.4, 2.2 4.8, 6.7, 8.4, 12.2, 22.0, (bw=500 MHz) | 26 | S,VLBI
 | Ceduna | 133.81º | -31.87º | 2.2, 4.8 , 6.7, 8.4, 12, 22.0, (bw=500 MHz) | 30 | S,VLBI
 | MOST | 149.42º | -35.37º | 841.5-844.5 M | 2 x (778m x 12m) | I
5 member adm.
- total 50 stations
- Australia(7)
- China (6)
- India (6)
- Japan (24)
- Korea (7)

## Slide 6
Regional Base
 Common proposal of each Regions
International Base  Registration with API (Advance publication of information )
National Base
 Consult with each administrations
WRC-12 (Geneva, 2012)
For RAS Protection

## Slide 7: Principal Tasks of APG meetings
5th meeting (Final)
- Develop APT common proposals for WRCs
WRC process
4th meeting
- Develop APT common proposals for CPM
e.g. CPM process
for WRCs
1st – 3rd meeting
- Develop APT Preliminary Views for WRCs

## Slide 8: Table of contents of the RAS related issues
WP | CPM Report Chapter | WRC-12 Agenda Items | Chairman
WP1 | Chapter 1: Maritime and Aeronautical Issues | 1.3, 1.4, 1.9, 1.10 | Mr. Darrell Ninham (Australia)
WP2 | Chapter 2: Radiolocation and Amateur Issues | 1.14, 1.15, 1.21, 1.23 | Prof. Ahmad Faizal Bin Mohd Zain (Malaysia)
WP3 | Chapter 3: Fixed, Mobile and Broadcasting Issues | 1.5, 1.8, 1.17, 1.20, 1.22 | Dr. Hyansuk Seong (Rep. of Korea)
WP4 | Chapter 4: Science Issues | 1.6, 1.11, 1.12, 1.16, 1.24 | Mr. Zhou Xingguo (P.R. China)
WP5 | Chapter 5: Satellite Issues | 1.7, 1.13, 1.18, 1.25, 7 | Mr. Muneo Abe (Japan)
WP6 | Chapter 6: Future Work Program and other Issues | 1.2, 1.19, 2, 4, 8.1, 8.2 | Mr. Taghi Shafiee (Islamic Republic of Iran)

## Slide 9: Coordination in APT
Part I General Status
Part II Related Issues

## Slide 10: Issue Items related to RAS
WRC AI | WP | APT Preliminary | APT Other Views | ITU-R Studies (2010.06) | Frq. bands
1.4 | 5B | O | X | 5B/238 | 112 – 117.975 MHz, 960 – 1 164 MHz 5 000 – 5 030 MHz
1.6 (Res.950) | 7C/7D 1A | O | O | 7C/158 7D/145 Annex 7, 1A/207 | 275 – 3000 GHz
1.8 | 5C | O | O | 5C/temp/229 | 71 - 238 GHz
1.11 | 7B | O | O | Annex 2, 7B/181 7B/185, 188, 191 5C/temp/217 | 22.55-23.15 GHz
1.13 | 4A | O | O | 4A/368N16 | 21.4-22 GHz
1.15 | 5B | O | X | 5B/235 | 3-50 MHz
1.19 | 1B | O | X | 1B/210N7 | SDR/CRS
1.20 | 5C | O | O | 5C/temp/221 | 5 850-7 075 MHz
1.21 | 5B | O | X | 5B/temp/234 | 15.4–15.7GHz
1.22 | 1A | O | O | 1A/252N7 | SRD
1.25 | 4C | O | O | 4C/436N20 5B | 4 - 16 GHz

## Slide 11: Issue Items related to RAS
Agenda Items ([ ] – low priority)
- 1.4, 1.6, 1.8, 1.11, [1.13], 1.15, 1.19, 1.20, 1.21, 1.22, 1.25
WP7D/SG7 is listed as a contribution group - AI 1.4, 1.6, 1.8, 1.19, 1.22, 1.25
WP7D/SG7 is listed as an interested group - 1.3, [1.5], 1.7, [1.10], [1.13], 1.14, 1.15, 1.20, 1.21

## Slide 12: WRC-12 AI 1.4
AI 1.4 to consider, based on the results of ITU-R studies, any further regulatory measures to facilitate introduction of new aeronautical mobile (R) service (AM(R)S) systems in the bands 112 – 117.975 MHz, 960 – 1 164 MHz and 5 000 – 5 030 MHz in accordance with Resolutions 413 (Rev.WRC-07), 417 [COM4/5] (WRC-07) and 420 [COM4/9] (WRC-07)
Continuation of WRC-07 agenda item 1.5

## Slide 13: APT Preliminary Views (APG12-3rd meeting, March 2010)
With regards to Resolution 420 (WRC-07), APT Members are of the view that it should first be studied to identify whether the spectrum requirements can be fulfilled in the band 5 091-5 150 MHz. Before considering new allocation in the band 5000-5030 MHz, it is necessary to demonstrate that AM(R)S would not create undue constraints on the Radio-Astronomy Service and existing radiocommunication services including Radio-Navigation Satellite Service.

## Slide 14: Draft CPM text (5B/temp/238) (May, 2010)
Method C1 – No changes to Article 5 of the Radio Regulations are required as a result of studies conducted within the ITU-R in response to Agenda item 1.4 Resolution 420 (WRC-07).
Method C2 – Add a primary aeronautical mobile (R) service allocation for 5 000-5 010 MHz, with no changes to the band 5 010-5 030 MHz, in the Table of Allocations of Article 5 of the Radio Regulations along with a Resolution that provides necessary measures to protect radionavigation satellite and radio astronomy services. Also suppress Resolution 420 (WRC-07).

## Slide 15
AI 1.6 to review No. 5.565 of the Radio Regulations in order to update the spectrum use by the passive services between 275 GHz and 3 000 GHz, in accordance with Resolution 950 (Rev.WRC-07), and to consider possible procedures for free-space optical-links, taking into account the result of ITU-R studies, in accordance with Resolution 955 [COM6/9] (WRC-07)
WRC-12 AI 1.6

## Slide 16
APT Members support to review No. 5.565 of the Radio Regulations and update the spectrum use by passive services in the range 275-3 000GHz, taking into account the results of ITU-R studies related to Resolution 950 (Rev.WRC-07).
APT Members also support studies to consider possible procedures for free-space optical links, in accordance with Resolution 955 (WRC-07).
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 17
One Member of APT is of the view that
a) The results of studies should not lead to monopolizing spectrum for passive services; recognizing an identification of possible use of certain bands for passive services should not preclude future consideration of these bands for active services. However, such identification should not be conditioned by identification for use by other services.
b) The on-going studies within the ITU-R should aim at, among other things, to the definition of passive services requirements. Such studies should lead to a revision of N° 5.565 that would refer to corresponding Resolutions
c) In connection with the regulatory methods to satisfy this agenda item (1.6/1) , both Methods are acceptable at this stage, since actually, Method B is similar to Method A which proposes, in addition to the Resolutions referenced in N° 5.565, also to include in RR 5.565 the list of frequency bands for passive services
OtherViews (APG12-3rd meeting, March 2010)

## Slide 18: WD Draft CPM text (1A/207N7) (Oct., 2009)
Method A – RR No. 5.565 would be modified to simply refer to relevant different resolutions that would address the use of frequency bands between 275 GHz and 3 000 GHz by EESS, SRS, radio astronomy and ground-based passive sensors
Method B – Lists of bands of interest to EESS, SRS, and RAS in the range 275-1 000 GHz would remain in RR No. 5.565 (with possible modifications). Interest of the passive services at all frequencies from 1 000-3 000 GHz would be added

## Slide 19
AI 1.8 to consider the progress of ITU-R studies concerning the technical and regulatory issues relative to the fixed service in the bands between 71 GHz and 238 GHz, taking into account Resolutions 731 (WRC-2000) and 732 (WRC-2000)
- Compatibility studies between the RAS and the FS. Studies may result in new regulatory measures in the RR. Contributions by the RAS are highly needed.
WRC-12 AI 1.8

## Slide 20
APT Members support ITU-R studies on the technical and regulatory issues to facilitate the technological developments and improve flexibility for FS in the FS allocations subject to the following conditions in the bands above 71GHz:
protection of the services to which frequency band is allocated;
no imposition/restriction on the development of the services
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 21
Some APT Members noted that there is no intention to extend the frequency allocations to the fixed service under this agenda item.
Some APT Members are of the views as follows:
- EESS in the band 86-92 GHz may be protected by unwanted emission masks on FS in the band 81-86 GHz. However, more consideration should be made to minimize burden on FS.
- RAS may be protected by non-LOS location or appropriate separation distance between RAS and FS stations on a national regulatory basis. Therefore, there is no need of regulatory measures in Radio Regulations.
APT Other Views (APG12-3rd meeting, March 2010)

## Slide 22: Draft CPM text (5C/temp/229) (May, 2010)
Method A1 – No changes to Article 5 of RR
Method A2 – NOC, continue ITU-R studies
Method B1 – apply a mandatory unwanted emission mask in the bands 81-86/92-95 GHz
Method B2 – apply a recommended unwanted emission mask in the bands 81-86/92-95 GHz.

## Slide 23
AI 1.11 to consider a primary allocation to the space research service (Earth-to-space) within the band 22.55-23.15 GHz, taking into account the results of ITU‑R studies, in accordance with Resolution 753 (WRC‑07)
WRC-12 AI 1.11

## Slide 24
APT Members support a primary allocation to the space research service (SRS) in accordance with Resolution 753 (WRC-07), provided that ITU-R sharing studies demonstrates compatibility with and protection of existing and future fixed, inter-satellite and mobile services within the band 22.55–23.15 GHz.
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 25
The Draft CPM text acknowledges the very high numbers of FS stations in many countries as backhaul to mobile phone base stations in the frequency band 22.55-23.15GHz.
One APT Member emphasized the need to ensure that regulatory measures (e.g. a minimum separation distance between SRS stations and the borders of neighbouring countries) are included in any WRC outcome to ensure protection of existing and future FS stations across borders of neighbouring countries.
APT Other Views (APG12-3rd meeting, March 2010)

## Slide 26: Draft CPM text (5C/temp/217) (May, 2010)
Method A – Make a primary allocation to the space research service in the band 22.55-23.15 GHz
[Method B – Make a primary allocation to the space research service in the band 22.55-23.15 GHz. However receiving SRS satellite systems shall not claim protection from, nor constrain the use and development, of stations of the fixed service in the band 22.55 – 23.15 GHz.]

## Slide 27
AI 1.13 to consider the results of ITU‑R studies in accordance with Resolution 551 (WRC‑07) and decide on the spectrum usage of the 21.4-22 GHz band for the broadcasting-satellite service and the associated feeder-link bands in Regions 1 and 3
WRC-12 AI 1.13

## Slide 28
Support the ITU-R studies
It is preferable to await the completion of the ITU-R studies before deciding which method would be the most appropriate for BSS applications in Region3.
−105 dB(W/(m2 · 1 MHz)) should be considered as the reference pfd at the Earth’s surface to be used in studies on sharing for the BSS in the band 21.4-22.0 GHz in Region 3.
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 29
Some APT Members have a view that with respect to the status of use of the band 21.4-22 GHz band in Regions 1 and 3, it is necessary that WRC-12 reconsider the matter and decides appropriately in the light of current and potential use of the frequency band 21.4-22 GHz for terrestrial services in Regions 1 and 3 with a view to providing equal status to terrestrial services in Regions 1 and 3 with respect to BSS in those Regions. Some APT Members emphasize that this view is not within the scope of this Agenda item 1.13.
Some APT members believe that currently there are some contradictions between 23.13A and 23.13B and such inconsistency need to be corrected as shown in the example text in Annex 2 below. Some APT Members emphasize that this view is not within the scope of this Agenda item 1.13.
APT Other Views (APG12-3rd meeting, March 2010)

## Slide 30: Draft CPM text (4A/temp/198) (March, 2010)
Method A – F
- now Developing in ITU-R WP4A
(Doc# /Annex 16 to Doc. 4A/368)
- next meeting July 2010

## Slide 31
AI 1.15 “to consider possible allocations in the range 3-50 MHz to the radiolocation service for oceanographic radar applications, taking into account the results of ITU‑R studies, in accordance with Resolution 612 (WRC‑07)”
- Make sure that the RAS bands don’t creep back into consideration for these radars.
WRC-12 AI 1.15

## Slide 32
APT Members support possible allocations, each band not exceeding 600 kHz, to suitable candidate sub-bands in the range 3-50MHz to the radiolocation service for oceanographic radar applications, provided that ITU-R sharing studies demonstrate the compatibility of the oceanographic radar applications with and the protection of existing services in accordance with Resolution 612(WRC-07).
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 33: Draft CPM text (5B/temp/235) (May, 2010)
Method A
Add new primary radiolocation allocations in RR Article 5 in all, some, or portions of the frequency bands 3 155-3 200 kHz, 4 438-4 650 kHz, 5 060-5 450 kHz, 7 450-8 100 kHz, 9 040-9 400 kHz, 9 900-9 995 kHz, 12 100-12 230 kHz, 13 410‑13 570 kHz, 13 870-14 000 kHz, 14 350-14 990 kHz, 15 800-16 350 kHz, 22 855‑23 200 kHz, 24 000-24 890 kHz, 25 010-25 070 kHz, 25 210-25 550 kHz, 26 175‑27 500 kHz, 39‑39.986 MHz, 40.02-40.98 MHz and 41.015-47 MHz
Method B - on a secondary basis to the RLS
Method C - on primary and/or secondary basis to RLS

## Slide 34: WRC-12 AI 1.19
AI 1.19 to consider regulatory measures and their relevance, in order to enable the introduction of software-defined radio and cognitive radio systems, based on the results of ITU-R studies, in accordance with Resolution 956 [COM6/18]
(WRC-07)
Cognitive radio systems use the method by which such systems would recognize the use of spectrum by passive services and avoid interference to them.

## Slide 35
1. APT Members are of the view that SDR and CRS are not radio services as listed in Article 1 of the Radio Regulations. In this connection, any specific frequency allocation using SDR or CRS technologies in the Radio Regulations is not necessary.
2. With respect to SDR, APT Members support the single method which has been identified by ITU-R WP 1B (No change to the Radio Regulations and suppress Resolution 956 (WRC-07)).
3. With respect to CRS, APT Members support Method B1 (No change to the Radio Regulations and suppression of Resolution 956 (WRC-07)).
4. APT Members are of the view that SDR and CRS may be operated under any radiocommunication services.
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 36: Draft CPM text (1B/210N7) (May, 2010)
Issue A: Software defined radios (SDR)
Method A: No change to the Radio Regulations
Issue B: Cognitive Radio Systems (CRS)
Method B1: No change to the Radio Regulations
Method B2: No change to the articles of the Radio Regulations and a Resolution providing guidance for further studies on CRS
Method B3: No change to the articles of the Radio Regulations and a Resolution dealing with the use of CRS and further studies within the ITU-R.

## Slide 37
AI 1.20 to consider the results of ITU‑R studies and spectrum identification for gateway links for high altitude platform stations (HAPS) in the range 5 850-7 075 MHz in order to support operations in the fixed and mobile services, in accordance with Resolution 734 (Rev.WRC‑07)
WRC-12 AI 1.20

## Slide 38
APT Members support ITU-R sharing studies for potential frequency identification of HAPS gateway links in the range 5 850-7 075 MHz which are already allocated to the fixed service, in accordance with Resolution 734 (Rev. WRC-07), on the condition of adequate protection of the existing and planned services and AP 30B Plan Allotment in this frequency band as contained in the Radio Regulations and BR database.
Furthermore, it should be ensured that no constraints or restrictions to be imposed to the deployment of AP 30B transmitting earth station due to the fact that such deployment is generally of VSAT type application within entire service area of AP 30B Plan assignment.
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 39
Other views from APT Members:
Some APT Members have a view that if HAPS gateway links are to be considered in the band 5 850-7 075 MHz, such operation shall be on non-harmful interference and non-protection basis with respect to GSO-FSS.
In addition, some APT Members have a view that it should be ensured that no constraints or restrictions to be imposed to the deployment of FSS due to the fact that such deployment is generally of VSAT type application within entire service.
Some other APT Members have a view that it is premature to introduce such conditions above before conclusion of ITU-R studies.
APT Other Views (APG12-3rd meeting, March 2010)

## Slide 40: Draft CPM text (5C/temp/221) (May, 2010)
Method A – No change to the 5 850-7 075 MHz band
existing identified spectrum in the bands 47.2-47.5 GHz and 47.9-48.2 GHz in RR No. 5.552A, 27.9-28.2 GHz and 31.0-31.3 GHz are also available for use by HAPS in the countries listed in RR No. 5.537A and 5.543A
Method B – new identification of two channels of 80 MHz for HAPS gateway links within the range of 5 850-6 725 MHz through a country footnote

## Slide 41
AI 1.21 to consider a primary allocation to the radiolocation service in the band 15.4–15.7GHz, taking into account the results of ITU‑R studies, in accordance with Resolution 614 (WRC‑07)
WRC-12 AI 1.21

## Slide 42
APT Members support consideration of a primary allocation to the radiolocation service in the band 15.4-15.7GHz only on the condition that the results of ITU-R studies between the radiolocation service and existing primary services in the band 15.4-15.7GHz together with the radio astronomy service in the adjacent band 15.35-15.40GHz shall not put undue constraints on services to which the frequency bands are currently allocated and in accordance with Resolution 614 (WRC-07).
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 43: Draft CPM text (5B/temp/234) (May, 2010)
Method [A/B]
The addition of a primary allocation for radiolocation in the [15.4-15.7]/[15.5/15.55-15.7] GHz band with any necessary regulatory provisions to protect the RAS in the 15.35-15.4 GHz band
ADD
5.B121 In order to protect the radio astronomy service in the band 15.35-15.4 GHz, radiolocation stations operating in the band 15.4-15.7 GHz shall not exceed the power flux-density level of –156 dB(W/m2) in a 50 MHz bandwidth into the band 15.35-15.4 GHz, at any radio astronomy observatory site for more than 2% of the time.

## Slide 44
AI 1.22 to examine the effect of emissions from short-range devices on radiocommunication services, in accordance with Resolution 953 (WRC-07)
the proliferation of short-range RF devices such as UWB and RFID tags, and the effect on existing radiocommunication services of these devices
WRC-12 AI 1.22

## Slide 45
1. APT Members expressed concerns of the impact of emissions from SRDs on radiocommunication services. Therefore they support the studies being carried out by ITU-R WP1A relating to the impact of emissions from SRDs on the operation of radiocommunication services to which the frequency bands are allocated in order to protect these services.
2. APT Members support the studies by ITU-R WP1B in accordance with the Resolution ITU-R 54 (“studies to achieve harmonization for short range radiocommunication devices (SRDs)”) which resolves to study and advise on a mechanism that may ease the use of relevant frequency bands and/or frequency tuning ranges, preferably on a global or regional basis, suitable for SRDs.
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 46
1. Some APT Members are of the view that method A should be supported, and of the view that Method B should also be given favorable consideration.
2. Some other APT Members are of the view that it is premature to select any method(s) at this stage.
3. Some APT Members are of the view that regulation of emissions by SRDs can be achieved via national arrangement using, when available, relevant ITU-R Recommendations or regional agreements.
APT Other Views (APG12-3rd meeting, March 2010)

## Slide 47: Draft CPM text (1A/252N7) (Feb., 2010)
Method A –Keep current practice
Method B –WRC General Resolution
WRC Resolution inviting the ITU-R to study the regional and global harmonization of certain SRDs
Method C: Recognize a limited number of harmonized tuning bands and emission levels for SRD applications either by a Resolution at WRC-12 or regulatory changes in Article 5 for SRDs similar to those specific bands for ISM
Method D: Provisions in the Radio Regulations
The Radio Regulations would contain a definition of SRDs and provisions for under what conditions they can operate

## Slide 48
AI 1.25 to consider possible additional allocations to the mobile-satellite service, in accordance with Resolution 231 (WRC-07)
- Resolution 231 invites the ITU-R to study the possibility of Additional allocations to the mobile-satellite service with the bands between 4 GHz and 16 GHz
WRC-12 AI 1.25

## Slide 49
1. APT Members support the completion of studies in the range 4GHz to 16GHz for any possible additional allocations to MSS, subject to not placing additional than those currently existing constraints on existing radiocommunication services operated in the existing allocated bands, as in accordance with Resolution 231 (WRC-07).
2. APT Members are of the view that prior to the additional allocations to the MSS in the frequency range specified, a technical compatibility between MSS and existing services in the bands should be taken into account as well, by which the existing services should have adequate protection from the additional allocations to the MSS.
APT Preliminary Views (APG12-3rd meeting, March 2010)

## Slide 50
Some APT Members are of the view that sharing spectrum between MSS and FS are very unlikely to be feasible, unless shown conclusively in ITU-R studies that existing FS services will not be adversely affected by this new identification.
The bands which are extensively used by FS are 4400-4500 MHz, 4800-4990 MHz, 7055-7250 MHz, 7750-7900 MHz, 8400-8500 MHz, 10.5-10.6GHz and 14.8-15.35 GHz.
APT Other Views (APG12-3rd meeting, March 2010)

## Slide 51: Draft CPM text (4C/436N20) (March, 2010)
Method
- now Developing in ITU-R WP4C
(Doc# /Annex 20 to Doc. 4C/436)
- next meeting July 2010
Frequency band | MSS direction (DL = downlink, UL = uplink)
5 150-5 250 MHz | DL
7 055-7 250 MHz | DL
8 400-8 500 MHz | UL
10.5-10.6 GHz | DL
13.25-13.4 GHz | DL
15.43-15.63 GHz | UL

## Slide 52: Role of APT
<number>
APT will harmonize regional views on standardization matters and present them at the relevant global forums (WRC, WTSA, WTDC etc.)

## Slide 53
Thank you!

## Slide 54: Asia-Pacific RA Telescopes-1
<number>
China
Radio astronomy stations operating in the Asia-Pacific Region |  |  |  |  |  | 
Country | Site | Longitude (East) | Latitude (North) | Operating Frequency (M/GHz) | Diameter (m) | Remarks
China | Shanghai | 121.2º | 31.1º | 1.62-1.68, 2.15-2.45, 4.7-5.1, 8.1-9.0, 22.1-22.6, Hz | 25 | S, VLBI
 | Urmuqi | 87.18º | 43.5º | 314-340 M, 605-615 M 1.38-1.70, 2.15-2.45, 4.75-5.15, 8.18-8.67, 22-24, Hz | 25 | S, VLBI
 | MSRT | 116º 58' | 40º 33' | 229-235 M | 28 x 9m | I
 | MIYUN50 | 116º 58' | 40º 33' | 229-235 M, 294.3-359.7 M 549.9-672.1 M 1-2, 2.07-2.53, 4.5-5.5, 7.56-92.4 , 3.5-16.5, Hz | 50 | S, VLBI
 | Delingha | 97º 44' | 37º 22' | 22-24, 85-120, Hz | 13.7 | S

## Slide 55: Asia-Pacific RA Telescopes-1
<number>
India

## Slide 56: Asia-Pacific RA Telescopes-1
<number>
Japan
Japan | Nobeyama | 138º 28' 32" | 35º 56' 29" | 1.4-1.427, 1.66-1.669, 4.7-5.14, 15.35-15.4, 20-24, 26-50, 72-116 | 45 | S
 | Nobeyama | 138º 28' | 35º 56' | 85 – 116, 126-152, 213-237, 325-365 | 10 x 6m | I
 | Nobeyama Heliograph | 138º 28' | 35º 56' | 17, 33.8 | 84 x 0.8m | I
 | Mizusawa | 141º 07' 56" | 39º 08' 00" | 2.15-2.35, 8.13-8.6, 19.5-25.0, 43-45 | 10 | S,VLBI
 | VERA-Mizusawa | 141º 07' 57" | 39º 08' 01" | 2.2-2.4, 8.1-9.0, 21.5-23.8, 42.5-44.5, 85-87 | 20 | S,VLBI
 | VERA-Kagoshima | 130º 26' 24" | 31º 44' 52" | 2.2-2.4, 8.1-9.0, 21.5-23.8, 42.5-44.5, 85-87 | 20 | S,VLBI
 | VERA-Ogasawara | 142º 13' 00" | 27º 05' 31" | 2.2-2.4, 8.1-9.0, 21.5-23.8, 42.5-44.5, 85-87 | 20 | S,VLBI
 | VERA-Ishigakijima | 124º 10' 06" | 24º 24' 38" | 2.2-2.4, 8.1-9.0, 21.5-23.8, 42.5-44.5, 85-87 | 20 | S,VLBI
 | Kashima | 140º 39' 58" | 35º 57' 03" | 1.45-1.75, 2.25-2.35, 4.6-5.1, 7.86-8.68, 10.2-10.7, 14.4-15.4, 21.9-22.4, 23.5-24.0, 42.9-43.4, | 34 | S
 | Usuda | 138º 21' 57" | 36º 07' 45" | 1.4-1.75, 2.2-2.3, 4.7-5.14, 8-9, 21.9-22.9, | 64 | S
 | Nishi-Harima | 133º 00' 41" | 33º 32' 39" | 18-250 M | ? | S
 | Toyokawa | 137º 22' 09" | 34º 50' 05" | 322-332 M | 1012 m2 | S
 | Fujigane | 138º 36' 42" | 35º 25' 36" | 322-332 M | 1500 m2 | S
 | Sugadaira | 138º 19' 16" | 36º 31' 12" | 322-332 M | 1100 m2 | S
 | Kiso | 137º 37' 49" | 35º 47' 34" | 322-332 M | 1405 m2 | S
 | Zao | 140º 31' 59" | 38º 06' 07" | 322-332 M | Four arrays | S
 | Hiraiso | 140º 37' 31" | 36º 22' 17" | 25-70 M,70-500 M,1.4-1.6, 2.8GHz | Log-periodic 10,6,2 | S S
 | Nishi-Waseda | 139º 43' 20" | 35º 42' 25" | 10.65, | 2.4 x 64 | S
 | Nasu | 139º 59' | 36º 55' 30" | 1.4, | 20 x 5 | S
 | Nagoya | 136º 58' | 35º 09' | 110-116, | 4 | S
 | Mt.Fuji | 138º 43' 38" | 35º 21' 44" | 325-350, 440-500, 800-830, | 1.2 | S
 | Tomakomai | 141º 36' 00" | 42º 40' 19" | 2, 8, 22, 43, | 11 | S,VLBI
 | Gifu | 136º 44' 22" | 35º 28' 03" | ? | 11 | S
 | Yamaguchi | 131º 33' 35" | 34º 12' 48" | ? | 32 | S

## Slide 57: Asia-Pacific RA Telescopes-1
<number>
Korea
Radio astronomy stations operating in the Asia-Pacific Region |  |  |  |  |  | 
Country | Site | Longitude (East) | Latitude (North) | Operating Frequency (M/GHz) | Diameter (m) | Remarks
Korea | Taejon | 127º 22' 18" | 36º 23' 54" | 43-175 G | 13.7 | S, VLBI
 | K-SRBL | 127.37º | 36.40º | 245, 410 M 1-18 G | 2 x 2m | S
 | KVN-Yonsei | 126º 56' 35" | 37º 33' 44" | 2-115 G | 20 | S, VLBI
 | KVN-Ulsan | 129º 15' 04" | 35º 32' 33" | 2-115 G | 20 | S, VLBI
 | KVN-Tamna | 126º 27' 43" | 33º 17' 18" | 2-115 G | 20 | S, VLBI
 | Seoul | 126º 57' 19" | 37º 27' 15" | 85-115G 200-270G | 6 | S
 | Ichon (RRL) | 127º 32' 58" | 37º 09' 01" | 30M-2.5G | 6, 10 | S