## Slide 1: Radio Quiet Zones
Carol Wilson, CSIRO
3rd Summer School in Spectrum Management for Radio Astronomy
31 May – 4 June 2010, Tokyo

## Slide 2: Outline of talk
What is a radio quiet zone?
Why are they needed?
Methods to achieve a radio quiet zone
Examples
Conclusions

## Slide 3: What is a Radio Quiet Zone?
“Prevention is always better than a cure.” Best strategy is to “prevent” RFI rather than mitigate it after the fact.
Radio Quiet  Radio Silent
RQZ = prevent “harmful” (detrimental) RFI
Various ways to achieve this – a combination of tools depends on frequency, telescope, location…
“…any recognized geographic area within which spectrum management procedures are modified to reduce or avoid interference to radio telescopes, thereby maintaining the required standards for quality and availability of observational data” WP 7D Draft New Report on RQZ

## Slide 4: Challenges in radio quietness protection
Range of potential interferers:
  Terrestrial licensed services (fixed, mobile, TV/radio, CB repeaters)
  Class-licensed services (mobile devices, short-range devices, etc)
  Aircraft and satellites
  Noise from non-communication systems (vehicles, households, industrial activity, power lines)
  On-site noise
Rigorous demands of radioastronomy
Time frame (telescope life of 50 years or more)
Technical + political + economic implications

## Slide 6: Extending the limits of science exploration
“Observations of significance in radio astronomy are those which result in new knowledge of astronomical phenomena, which either require making observations of objects not previously studied, or observing known objects with increased precision. Both such cases call for observations at the highest achievable sensitivity. As radio astronomy has matured, the usefulness of data which is limited in accuracy by the presence of interference has declined, and it is the usual practice of astronomers to delete data for which there is any evidence of interference.” Rec. ITU-R RA.1513-1

## Slide 7: Interference thresholds

## Slide 8: ITU-R Question & Report
Question in WP7D to initiate studies
  Characteristics of existing RQZ?
  RAS characteristics stimulating RQZ?
  Environment characteristics stimulating RQZ?
ITU-R Correspondence Group
  Inputs from many countries
  New Draft Report – comprehensive
  Finalised in 2010 (?)
    WP7D meetings; June and October 2010
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 9: Methods to achieve a RQZ
Geographic location – remote
Site shielding
Control of interference sources
  Notification, coordination, restriction (intentional radio devices)
  Physically control access to site
  Legislative control of activities near site (industrial, mining, use of electrical appliances, etc)
  Provide alternative technology to replace interference source
Requires commitment from government and ongoing maintenance.

## Slide 10: Choosing a quiet site to start with!
Sydney
Pop. 4 million
Narrabri
Pop. 6,000
Murchison
Pop. 4
40dB ?
Measurements with a
swept spectrum analyser

## Slide 11: Greenbank NRQZ
The original RQZ - model
1956 – West Virginia Radio Astronomy Zoning Act
  Graded EMC restrictions to 10 miles
1958 – NTIA & FCC National RQZ
  34000 sq km area
  Coordination of all Tx with RA telescope
Excellent protection in practice
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 12: Examples of national RQZs
Arecibo PRCZ – Puerto Rico & islands
  Natural site shielding by surrounding hills
  Coordination Zone
Jodrell Bank & other European telescopes
  Mainly EMC (local) & some National coordination
GMRT
  EMC – 10 km (light)30 km (heavy industry)
  National coordination up to 400 km (bands)
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 13: ALMA Quiet Zone -- Chile
Central Quiet zone: 30 km radius, no transmitters in ALMA bands (variously 31 to 950 GHz)
120 km radius coordination zone
  AUI/ESO may comment on xmit applications
    > 31 GHz, comply with 769 at site boundary
    < 31 GHz, 769 + limit on transmitter power
      EIRP such that pfd at ALMA border <2x10-6 W/m2
Formal recognition is needed to avoid future changes in policy.
Need to educate the general public and politicians about radio astronomy and the need for radio quiet zone.
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 14: “Radio sensitive zones” in Australia
Radio Act review 2002 – “radio sensitive zones”
  Notification and coordination - no protection
Regulatory RALI (2006) covers all Oz RA sites (MS31)
Studies by ACMA (administration)
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 15: Notification Zone Parameters
Limits derived from RA.769 (+ ~10-15 dB) & VLBI
Propagation models from P.526 (Diffraction) and terrain models.
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 16: RALI MS 32 distances and thresholds
Restricted – no new apparatus licences (except in extraordinary cases)
Coordination – if power at MRO is above threshold, consultation with CSIRO required

## Slide 17: RALI MS 32 distances
100-230 MHz coordination
100-230 MHz restricted
>230 MHz restricted

## Slide 18
Comment on the SKA RQZ in Australia in a speech by the chairman of the Australian Communications and Media Authority:
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 19: Conclusions
Radio Quiet Zone increasingly important for existing and (especially) new radiotelescopes to extend science goals
Number of mechanisms, procedures to address different types of interference
Starting with a naturally quiet site simplifies both technical and regulatory problems
Important to work with national and local authorities and with the community.

## Slide 20: Thank you! Questions?
Contact Us
Phone: 1300 363 400 or +61 3 9545 2176
Email: enquiries@csiro.au Web: www.csiro.au
Carol Wilson, Research Consultant
carol.wilson@csiro.au