## Slide 1
07/31/26
<number>
Tomas E. Gergely
National Science Foundation
Third Summer School in Spectrum Management for Radio Astronomy
NAOJ, Tokyo, Japan
June 4, 2010
Notes: <number>

## Slide 2: Beginnings
Hertz experiments (1885-1889) show the existence of radio waves. - "This is just an experiment that proves Maestro Maxwell was right - we just have these mysterious electromagnetic waves that we cannot see with the naked eye. But they are there."
- "So, what’s next?"
- "Nothing, I guess."
  Maritime Communications - “ Someday lightships might use microwave beams to overcome the problem of fog interfering with shore communication” - The Electrician (London), 1891)
  First International Regulations: 1906 Berlin Conference (INTERNATIONAL WIRELESS TELEGRAPH CONVENTION) - First “allocations” – to shipboard stations: λ = 300 m or 600 m
  Invention of the Audion Tube- Lee de Forest (1913) “De Forest has said in many newspapers and over his signature that it would be possible to transmit human voice across the Atlantic before many years. Based on these absurd and deliberately misleading statements, the misguided public . . . has been persuaded to purchase stock in his company.” New York District Attorney at Lee de
  Forests’ fraud trial.
  1932 K. Jansky detects cosmic radio emission (searching for the origin of interference in ship to shore communications) Experimental frequency allocations made up to……300 MHz
<number>

## Slide 3: Radio Astronomy Interference Concerns
1930 to early 1980s
Stationary or slowly moving sources of interference
1982 to late 1990s
NGSOs
2000 to……
Mobile, broadband, wireless applications
07/31/26
<number>

## Slide 4: K. Jansky to NGSOs (1932-1982)
07/31/26
<number>
Consider a....
Radio telescope (ideally a single dish) at a well defined location, observing in a radio astronomy band
and an interferor
One (or more) transmitter(s) at well defined location(s) or slowly moving, radiating co-frequency
or in a neighboring band
Notes: <number>

## Slide 5: Solution(s)
07/31/26
<number>
Geographical separation-
Locate radio telescope:
  As far as possible from human activity
  In quiet/coordination zones
Regulations (national and international)
  Table of allocations
  ITU-R Recommendations
Technical
  e.g. Null in the direction of the telescope
Throw out bad data, hand selected
(Hopefully a small amount, but not quantified)
Notes: <number>

## Slide 6: After 1982 - NGSO Satellites
considering f) that while frequencies for communication with objects in extraterrestrial space are being selected at present on the basis of particular communication requirements and technological capabilities, the inevitable increase in this type of communication is likely to lead to a chaotic situation in the radio spectrum; ( CCIR Rec. 259, Los Angeles, 1959)
Constellations of Non-geostationary satellites (NGSOs)
LEOs, MEOs, HEOs
Global, 24 hr coverage
Rapidly moving
Multiple beams
Multiple, simultaneous
signals
Examples: GPS, Glonass,
Iridium, Globalstar
07/31/26
<number>
Notes: <number>

## Slide 7: Problems with NGSO Satellites
07/31/26
<number>
“Traditional” solutions no longer work
  Locate radio telescopes
    far from human activity
    in quiet/coordination zones
  Throw out bad data
Permanently deny access to some bands
  e.g. GPS 1544-1559 MHz; Iridium 1621.35-1626.5 MHz
Problems frequently spill over into other (sometimes distant) bands!
  e.g. “old” GLONASS satellites
Notes: <number>

## Slide 8: Solution(s)
Regulation (national and international)
  Allocations:
    Attempts to locate satellite downlink allocations far from
    radio astronomy bands (successful above 70 GHz )
  Place regulatory limits on unwanted emissions -
    General case: ITU Task Groups (TG 1/3, 1/5, 1/7 and 1/9 )– huge amount of effort and expense over 10 years- little (but some!) progress
    Particular case: In several cases mandatory limits on emission into neighboring bands through footnotes to the RR
  Recommendations (Non-mandatory) :
    Coordination – largely voluntary- outcome of last couple of WRCs ( Resolution 739)
    Recommendation on acceptable percentage of data loss to radio astronomy (Rec. ITU-R RA.1513)
    Developed methodology to calculate threshold levels of interference by NGSOs
  International Quiet Zones
    Adamantly opposed by some/most Administrations (U.S., Canada),
  Mitigation
07/31/26
<number>

## Slide 9: 2000 – Present: Unlicensed- Mobile - Broadband Growth
07/31/26
<number>
X
Global Mobile IP traffic is projected to grow at a combined (use X users) annual growth rate of 131% (Cisco)
Average mobile broadband subscriber is expected to consume (per month) 55 MB email, 2.7 GB Internet Radio, 9 GB video, and 27 GB HD movies (2008, Rysavy Research)
If laptops are included monthly mobile traffic escalates (per user) from 1GB per month in 2009 to 14 GB per month in 2015 (Cisco)
UWB: Systems that use extremely short-duration pulses or high chip rates to generate wideband (up to or greater than 1 GHz wide) signals
    Many Popular Applications: imaging (ground penetration, in-wall, through-wall, & medical), field disturbance (perimeter security, fluid level diagnostics…), communications (high data rate, high security, good interference immunity), radar (including vehicular radar)
Notes: <number>

## Slide 10: Science Requirements
Increasingly, radio astronomers desire access to the whole spectrum.
Increase in sensitivity and desire
to observe fainter sources
Increased access to spectral lines e.g. Deuterium, at 327.384 MHz, detected in 2005, Helium (3He+) at 8 665.650 MHz, Methanol (CH3OH) at 12.178 GHz
High Redshift
07/31/26
<number>
HI line
z = 0 0 Gyr ƒ (H0) = 1420 MHz
z = 1 ~ 8 Gyr 710 MHz
z = 3 ~ 11,5 Gyr 355 MHz
z = 10 ~ 13 Gyr 129 MHz
Universal expansion shifts spectrum
Spectra of objects farther away are shifted more
Shift gives the distance and look-back time
Notes: <number>

## Slide 11: Ap. J. June 10, 2010 Issue Radio Astronomy Papers
Telescope | Country | Band of Observation (GHz) | Bandwidth (GHz) | Allocations
RATAN 600 | Russia | 0.95; 2.3;4.8;7.7;11.2; 21.7 | 0.03,0.25,0.6,1.0, 1.4,.2.5 | Fixed Mobile Broadcasting Radiolocation Radionavigation Fixed Satellite Service (space-to- Earth) Broadcasting Satellite Service Fixed Satellite Service (Earth-to-space) Broadcasting Satellite Service
VLA | USA | 1.4; 5.0; 8.0; 22.0 |  | 
Effelsberg | Germany | 2.64;4.85;8.35;10.45;14.6;23.05;32.0;42.0 |  | 
Parkes | Australia | 0.732;1.374;3.100 | 64;256;1024 | 
OVRO | USA | 15.0 | 3.0 | 
SZA (2 papers) | USA | 31.0; 81.0-99.0 |  | 
AmiBa | China | 84.0-104.0 | 10.0 | 
CARMA | USA | 107.5-107.7, 111.5-111.7 |  | 
07/31/26
<number>
Radio astronomy observations appear to be carried out in all ITU Regions, in bands occupied by other services, some of them transmitting at high power!

## Slide 12: Reality vs. Regulations
07/31/26
<number>
Older, single dish telescopes, (e.g. Effelsberg, Arecibo), usually have narrowband receivers, that cover or overlap allocated radio astronomy bands
Increasingly, however, the tendency is towards building broadband receivers, that are required by the science, without regard to allocations e.g. EVLA 1-50 GHz, LOFAR (30-240 MHz)
In terms of spectrum, regulations may only cover/protect relatively narrow bands (except, possibly, at mm wavelengths) allocated to radio astronomy
This is true for
    “hard” regulations (the Radio Regulations)
    “soft” regulations (ITU-R Recommendations)
As a rule, regulations reference Recommendation ITU-R RA.769
  However, Rec. RA.769 refers to an idealized observation, and while it is a good criterion, compliance will NOT necessarily protect some observations (e.g. long integrations or pulsar observations)
Notes: <number>

## Slide 13: Observing outside allocated bands Are there rights/protections for out-of-band allocations?
07/31/26
<number>
Art. 29 (29.8)
The status of the radio astronomy service in the various frequency bands is specified in the Table of Frequency Allocations (Art. 5). Administrations shall provide protection from interference to stations in the radio astronomy service in accordance with the status of this service in those bands (see also Nos. 4.6, 22.22 to 22.24 and 22.25).
Art. 4 (4.6)
For the purpose of resolving cases of harmful interference, the radio astronomy service shall be treated as a radio communication service. However, protection from services in other bands shall be afforded the radio astronomy service only to the extent that such services are afforded protection from each other.
Art. 22 (22.22 – 22.25)
Prohibits emissions causing harmful interference to radio astronomy in the Shielded Zone of the Moon, except for certain transmissions. Leaves the determination of what constitutes harmful inference up to agreements between Administrations
However:
Article 11(11.12)
Any frequency to be used for reception by a particular radio astronomy station may be notified if it is desired that such data be included in the Master Register.
Notes: <number>

## Slide 14: Observing outside allocated bands revisited- (Rec. ITU-R 314)
07/31/26
<number>
considering
b) that the advancement of radio astronomy requires the protection of certain frequency bands from interference;
d) that radio astronomers study spectral lines both in bands allocated to the radio astronomy service and, as far as spectrum usage by other services allows, outside the allocated bands, and that this has resulted in the detection of more than 3 000 spectral lines;
recommends:
3. that administrations be asked to provide assistance in the coordination of observations of spectral lines in bands not allocated to radio astronomy
Notes: <number>

## Slide 15: - Conclusion
- The existing regulatory regime does not satisfy fully radio astronomers requirements!
- The same can be said of a number of other communication services!
Questions
Are (Exclusive/Primary) radio astronomy bands (still) needed? Worldwide?
Do/ can passive bands satisfy the requirements of both the EESS and RA communities? Should these interests be separated?
Should the radio astronomy community make an attempt to trade its exclusive/primary allocations for a high level (Rec. 769 ) of protection across most of the spectrum, at a few locations worldwide ( ALMA, SKA, eVLA, etc. ) worldwide?
07/31/26
<number>

## Slide 16
Giving up Radio Astronomy Bands
Is Not Likely to Be the Answer!
From
D. Staelin
April 2010
A
B
Comm, doubling annually
Communications
6 months later
Science, etc.
Conversely, if Science doubled, communications capacity would again shift only ~one month
  Science utilization: Roughly proportional to number of scientists, ~ steady
Communications: Exponential growth
Consider a spectral region where communications double annually
- If communications occupies 2/3 and other users yield to communications, others would shrink from “A” to “B”
-Yielding buys only six months before communications becomes 100%;
science uses might represent only one month of growth.
Notes: <number>

## Slide 17: The Future
Radio astronomers will have develop/take advantage of
  appropriate interference mitigation techniques (and use them)
  Cognitive radio techniques (observing in unused spectrum)
  Dynamic spectrum access/ Cooperative Spectrum Usage
  Some of these issues are beginning to be explored, see e.g.
  “Spectrum Management for Science in the 21st Century”
  National Research Council, Washington, DC, 2010
  “ Nascent technologies exist for cooperative spectrum usage, but standards and protocols (regulation) do not” (p. 186)
  Regulations when they exist, (or future) are considered NATIONAL regulatory issues – not very helpful to passive services (and often, not even to active services)
07/31/26
<number>

## Slide 18: Backup Slides
07/31/26
<number>

## Slide 19: Detrimental Interference Levels at Radio Telescopes as Specified in Rec. ITU-R RA.769
07/31/26
<number>
Depend On:
Bandwidth (Sp lines)
  10 kHz; f<1 GHz
  20 kHz ; f< 5 GHz
  50 kHz ; f<22 GHz
  (for continuum)
  Allocated Bandwidth
Integration Time
  2000 sec
System Temperature
Antenna Response Pattern
  G= 32-log dBi 1o<<19o
  G = 0 dBi 19o<<180o
Are Independent of:
Collecting Area
Notes: <number>

## Slide 20: Rec. ITU-R RA.769 vs. Some New Telescopes
07/31/26
<number>
Notes: <number>

## Slide 21: Frequency Coverage
07/31/26
<number>
Single Dish Telescopes
MPI 100-m Telescope
  800 - 1700 MHz
  13 - 36 GHz
  40 - 50 GHz
Arecibo 305-m
  1120 - 1730 MHz
  1800 - 3100 MHz
  3950 - 6050 MHz
  8 - 10 GHz
GBT
  680 - 920 MHz
  1150 - 2600 MHz
  3950 - 5850 MHz
  8000 - 10100 MHz
  12 - 15.4 GHz
  18 - 26.5 GHz
LMT
  70 – 350 GHz
Sardinia Telescope
  0.3 to 100 GHz
Interferometers
EVLA
  1 – 50 GHz
ATA
  0.5 - 11.2 GHz
ALMA
  30 - 40 GHz
  Continuous coverage:
  ~67 – 950 GHz
Mileura WFA
  80 - 1400 MHz
LOFAR
  30 - 240 MHz
SKA
  100 MHz – 20 GHz
Notes: <number>

## Slide 22
Annual Doubling of Mobile IP is Forecast
D. Staelin
April 2010
<number>
Global Mobile IP Traffic Will Grow at a CAGR of 131 Percent
Growth = Users x Use
Use growth
Data
P2P
Video
Audio
Exabytes/month
2.5
2
1.5
1
0.5
0
Source: Cisco VNI, 2009
Growth is enabled by Moore’s law
Exabytes/month
60
30
0
Mobility
Business IP
Consumer IP
Consumer TV
What if last 2 meters are wireless?
Notes: <number>

## Slide 23: Observing Outside Radio Astronomy Bands
07/31/26
<number>
Detection of a radio counterpart to the 27 December 2004 giant flare from SGR 1806-20, by Cameron, P.B., Chandra, P., Ray,A., Kulkarni, S.R., Frail, D.A., Wieringa, M.H., Nakar,Phinney, E.S., Miyazaki,A, Tsuboi, M., Okukura, S., Kawai, N., Menten, K.M.,and Bertoldi, F, in Nature, 434, p.1112, 2005
327 MHz
1420 MHz
2290 MHz
4990 MHz
?
Notes: <number>

## Slide 24: Observing Outside Radio Astronomy Bands (2)
07/31/26
<number>
Frequency of RA Observation | Observatory | Band (MHz) | Allocated Services
240 MHz | GMRT | 235-267 | Fixed, Mobile (may be used by the MSS- Fn 5.254)
610 MHz | GMRT | 608-614 | Radio Astronomy - shared
1460 MHz | VLA, ATCA, GMRT | 1452-1492 | Fixed, Mobile exc. aeronautical mobile, Broadcasting, Broadcasting Satellite
2400 MHz | ATCA | 2300-2450 | Fixed, Mobile, Radiolocation, amateur
4860 MHz | VLA, ATCA | 4800-4990 | Fixed, Mobile, radio astronomy
8460 MHz | VLA, ATCA | 8400-8500 | Fixed, Mobile, Space Research (space-to-Earth)
102 GHz | NMA | 100-102 102-105 | Passive Fixed, Mobile exc. aeronautical mobile, Radio Astronomy
Notes: <number>

## Slide 25: Detrimental Threshold Levels vs. Frequency (Rec. ITU-R RA.769)
07/31/26
<number>
Threshold values of spectral power flux density for continuum (crosses) and spectral line (circles) plotted as a function of frequency (Rec. ITU-R RA.769).
Notes: <number>

## Slide 26: RFI and arrays
07/31/26
<number>
For closely spaced arrays, RFI is determined by the frequency of fringe oscillations at the output of two antennas
VLBI Interference is completely decorrelated
For detailed analysis, see:
  ITU Handbook on Radio Astronomy
  Interferometry and Synthesis in RA, Thompson, Moran and Swenson
  Attenuation of RFI by Interferometric Fringe Rotation, R. Perley, EVLA Memo 49
Interferometers attenuate RFI by factors of ~ 15 - 35 dB,
depending on: Integration time
        Frequency
        Baseline
        Source Elevation
Complicated situations, such as the SKA, demand a detailed analysis, and possibly several detrimental interference levels:
  a) for compact core, distributed between 1 km diameter and 150 km diameter, and
  b) far away stations, located up to 3000 km from the core
Notes: <number>

## Slide 27: Rec. ITU-R RA.769 vs. New Telescopes
07/31/26
<number>
Notes: <number>